## Slide 1
SFRs

## Slide 3: The ACC – Accumulator
Commonly used for move and arithmetic instructions.
Can be referred to in several ways:
  Implicitly in op-codes.
  Referred to as ACC (or A) for instructions that allow specifying a register.
  By its SFR address 0E0H.
Operates in a similar manner to the 8085 accumulator.
Bit addressable.
  ACC.2 means bit 2 of the ACC register.

## Slide 4: The B Register
Commonly used as a temporary register, much like a 9th R register.
Used by two op-codes
  MUL AB, div AB
B register holds the second operand and will hold part of the result
  Upper 8 bits of the multiplication result
  Remainder in case of division.
Can also be accessed through its SFR address of 0F0H.
Bit addressable.

## Slide 5: The DPL and DPH Registers
2 8-bit registers that can be combined into a 16-bit DPTR – Data Pointer.
Used by commands that access external memory
Also used for storing 16bit values
mov DPTR, #data16
; setup DPTR with 16bit ext address
movx A, @DPTR
; copy mem[DPTR] to A
Can be accessed as 2 separate 8-bit registers if needed.
DPTR is useful for string operations and Look-Up-Table (LUT) operations.

## Slide 6: The SP Register
SP is the stack pointer.
SP points to the last used location of the stack.
  Push operation will first increment SP and then copy data.
  Pop operation will first copy data and then decrement SP.
In 8051, stack grows upwards (from low memory to high memory) and can be in the internal RAM only.
On power-up, SP points to 07H.
  Register banks 2,3,4 (08H to 1FH) form the default stack area.
Stack can be relocated by setting SP to the upper memory area in 30H to 7FH.
  mov SP, #32H

## Slide 7: The PSW Register
Program Status Word is a “bit addressable” 8-bit register that has all the flags.
MSB |  |  |  |  |  |  | LSB
CY | AC | F0 | RS1 | RS2 | OV | - | P
Symbol | Position | Function
CY | PSW.7 | Carry Flag
AC | PSW.6 | Auxiliary Carry Flag. For BCD Operations
F0 | PSW.5 | Flag 0. Available to the user for general purposes.
RS1 | PSW.4 | Register bank select bits. Set by software to determine which register bank is being used.
RS2 | PSW.3 | 
OV | PSW.2 | Overflow Flag
- | PSW.1 | Not used
P | PSW.0 | Parity Flag. Even Parity. P=1 A contains an odd no. of 1’s

## Slide 8: The P0, P1, P2, and P3 Registers
Port Latches.
Specify the value to be output on the specific output port or the value read from the specific input port.
Bit addressable.
  First bit has the same address as the register.
  Example: P1 has address 90H in the SFR, so
    P1.7 or address 97H refer to the same bit.
Link: SFR address

## Slide 9: The SBUF Register
Serial Port Data Buffer.
2 registers at the same location
  One is read-only used for reading serial input data.
    Serial Data Receive Buffer.
  The other is write-only used for storing serial output data.
    Serial Data Transmit Buffer.
Link: SFR address

## Slide 10: Timer Registers – TH0 and TL0
The high and low bytes of the 16-bit counting register for timer/counter T0.
There is also a TH1 / TL1 pair for the T1 timer.
In the 8052, one more pair exists (TH2) / (TL2) for the T2 timer.
Link: SFR address

## Slide 11: Control Registers
IP – Interrupt Priority.
IE – Interrupt Enable.
TMOD – Timer Mode.
TCON – Timer Control.
T2CON – Timer 2 Control (8052)
SCON – Serial Port Control.
PCON – Power Control (80C51).
Link: SFR address

## Slide 12: 8051 – Timer /counter

## Slide 13: 8051 – Timer / Counter
2 – 16 bit timer / counter
4 – 8 bit registers – or 2 16 bit registers
TL0, TH0 – Timer/ Counter 0 and
TL1, TH1 - Timer/ Counter 1
  MOV TL0, #0FEH – instructions to load the counter
Can be used in 4 different modes
TMOD – Timer Mode selection register
TCON – timer control register
Timer operations can be controlled either by software or by hardware

## Slide 14: TCON – special function register
TCON – is a dual purpose register
Higher 4 bits D7- D4 – are timer control
Lower 4 bits are for interrupt control

## Slide 15
IE1 – external Interrupt 1 – edge flag – high to low edge coming to this external input will set this flag
  Reset when it jumps to ISS @ 0013H or by software
IT1 – external interrupt 1 signal type control
  It decides high to low edge or low level for interrupting the processor
IE0 – external Interrupt 0 – edge flag – high to low edge coming to this external input will set this flag
  Reset when it jumps to ISS @ 0003H or by software
IT0 – external interrupt 1 signal type control
  It decides high to low edge or low level for interrupting the processor

## Slide 16
The various bits of TCON are as follows.
TF1 : Timer1 overflow flag. It is set when timer rolls from all 1s to 0s. It is cleared when processor vectors to execute ISR located at address 001BH. TR1 : Timer1 run control bit. Set to 1 to start the timer / counter. TF0 : Timer0 overflow flag. (Similar to TF1) but vectors to execute ISR located at address 000BH TR0 : Timer0 run control bit. IE1 : Interrupt1 edge flag. Set by hardware when an external interrupt edge is detected. It is cleared when interrupt is processed. IE0 : Interrupt0 edge flag. (Similar to IE1) IT1 : Interrupt1 type control bit. Set/ cleared by software to specify falling edge / low level triggered external interrupt. IT0 : Interrupt0 type control bit. (Similar to IT1) As mentioned earlier, Timers can operate in four different modes.

## Slide 17: TMOD – Timer Mode Register
Lower 4 bits for Timer 0
Higher 4 bits for Timer 1
M0/ M1 – mode of operations of timer are decided
Gate and C/T(bar) – decides the control of operation either by software or hardware (interrupt)

## Slide 18
8051 Clock and Instruction Cycle
In 8051, one instruction cycle consists of twelve (12) clock cycles. Instruction cycle is sometimes called as Machine cycle by some authors.
In the "timer" function mode, the counter is incremented in every machine cycle.
Thus, one can think of it as counting machine cycles. Hence the clock rate is 1/12 th of the oscillator frequency.

## Slide 20: TMOD-
C/T – to define the source of input
  1 – source is from external
  0 – source is internal
GATE – defines the activation - enabling and disabling of count operation – by software or hardware means
Enabling and disabling by software and hardware means
Software control – GATE = 0
Hardware control GATE – 1 – interrupt will control the operation of timer

## Slide 21: 8051 Timer Modes
*
TE IT SEM-V
21
Timer 0
Mode 3
Mode 2
Mode 1
Mode 0
Mode 2
Mode 1
Mode 0
Timer 1
8051 TIMERS

## Slide 22
OSC
÷12
TL0
TH0
INTERRUPT
TIMER 0
TF0
*
22
TE IT SEM-V

## Slide 23
TL0
(5 Bit)
INTERRUPT
TIMER 0 – Mode 0
OSC
÷12
TH0
(8 Bit)
TF0
13 Bit Timer / Counter
Maximum Count = 1FFFh (0001111111111111)
*
23
TE IT SEM-V
The lower 5 bits of TLX and 8 bits of THX are used for the 13 bit count.
Upper 3 bits of TLX are ignored.
When the counter rolls over from all 0's to all 1's, TFX flag is set and an interrupt is generated.

## Slide 24
TL0
(8 Bit)
INTERRUPT
TIMER 0 – Mode 1
TH0
(8 Bit)
TF0
16 Bit Timer / Counter
Maximum Count = FFFFh (1111111111111111)
*
24
TE IT SEM-V
OSC
÷12
This mode is similar to mode-0 except for the fact that the Timer operates in 16-bit mode.

## Slide 25
TH0
(8 Bit)
Reload
TIMER 0 – Mode 2
8 Bit Timer / Counter with AUTORELOAD
TL0
(8 Bit)
OSC
÷12
TH0
(8 Bit)
TF0
INTERRUPT
Maximum Count = FFh (11111111)
*
25
TE IT SEM-V

## Slide 26
TL0
(8 Bit)
INTERRUPT
TIMER 0 – Mode 3
OSC
÷12
TF0
Two - 8 Bit Timer / Counter
OSC
÷12
TH0
(8 Bit)
INTERRUPT
TF1
*
TE IT SEM-V
Separate 2 8-bit counters
Timer 1 can be used only in mode 2 where TF1 and TR1 are not required
Control bits TR1 and TF1 are used by Timer-0 (higher 8 bits)
(TH0) in Mode-3
while TR0 and TF0 are available to Timer-0 lower 8 bits(TL0).

## Slide 27
OSC
÷12
TL1
TH1
INTERRUPT
TIMER 1
TF1
*
27
TE IT SEM-V

## Slide 28
TL1
(5 Bit)
INTERRUPT
TIMER 1 – Mode 0
OSC
÷12
TH1
(8 Bit)
TF1
13 Bit Timer / Counter
Maximum Count = 1FFFh (0001111111111111)
*
28
TE IT SEM-V

## Slide 29
TL1
(8 Bit)
INTERRUPT
TIMER 1 – Mode 1
OSC
÷12
TH1
(8 Bit)
TF1
16 Bit Timer / Counter
Maximum Count = FFFFh (1111111111111111)
*
29
TE IT SEM-V

## Slide 30
TH1
(8 Bit)
Reload
TIMER 1 – Mode 2
8 Bit Timer / Counter with AUTORELOAD
TL1
(8 Bit)
OSC
÷12
TH1
(8 Bit)
TF1
INTERRUPT
Maximum Count = FFh (11111111)
*
30
TE IT SEM-V

## Slide 31
8051 has about 111 instructions. These can be grouped into the following categories
Arithmetic Instructions Logical Instructions Data Transfer instructions Boolean Variable Instructions Program Branching Instructions
8051 Instruction set

## Slide 32
Mnemonics | Description | Bytes | Instruction Cycles
ADD A, Rn | A = (A + Rn) | 1 | 1
ADD A, direct | A A + (direct) | 2 | 1
ADD A, @Ri | A A + @Ri | 1 | 1
ADD A, #data | A A + data | 2 | 1
ADDC A, Rn | A A + Rn + C | 1 | 1
ADDC A, direct | A A + (direct) + C | 2 | 1
ADDC A, @Ri | A A + @Ri + C | 1 | 1
ADDC A, #data | A A + data + C | 2 | 1
DA A | Decimal adjust accumulator | 1 | 1
DIV AB | Divide A by B A quotient B remainder | 1 | 4
DEC A | A A -1 | 1 | 1
DEC Rn | Rn Rn - 1 | 1 | 1
DEC direct | (direct) (direct) - 1 | 2 | 1
DEC @Ri | @Ri @Ri - 1 | 1 | 1
INC A | A A+1 | 1 | 1
INC Rn | Rn Rn + 1 | 1 | 1
INC direct | (direct) (direct) + 1 | 2 | 1
INC @Ri | @Ri @Ri +1 | 1 | 1
INC DPTR | DPTR DPTR +1 | 1 | 2
MUL AB | Multiply A by B A low byte (A*B) B high byte (A* B) | 1 | 4
SUBB A, Rn | A A - Rn - C | 1 | 1
SUBB A, direct | A A - (direct) - C | 2 | 1
SUBB A, @Ri | A A - @Ri - C | 1 | 1
SUBB A, #data | A A - data - C | 2 | 1
Arithmetic instruction

## Slide 33
Mnemonics | Description | Bytes | Instruction Cycles
ANL A, Rn | A A AND Rn | 1 | 1
ANL A, direct | A A AND (direct) | 2 | 1
ANL A, @Ri | A A AND @Ri | 1 | 1
ANL A, #data | A A AND data | 2 | 1
ANL direct, A | (direct) (direct) AND A | 2 | 1
ANL direct, #data | (direct) (direct) AND data | 3 | 2
CLR A | A 00H | 1 | 1
CPL A | AA | 1 | 1
ORL A, Rn | A A OR Rn | 1 | 1
ORL A, direct | A A OR (direct) | 1 | 1
ORL A, @Ri | A A OR @Ri | 2 | 1
ORL A, #data | A A OR data | 1 | 1
ORL direct, A | (direct) (direct) OR A | 2 | 1
ORL direct, #data | (direct) (direct) OR data | 3 | 2
RL A | Rotate accumulator left | 1 | 1
RLC A | Rotate accumulator left through carry | 1 | 1
RR A | Rotate accumulator right | 1 | 1
RRC A | Rotate accumulator right through carry | 1 | 1
SWAP A | Swap nibbles within Acumulator | 1 | 1
XRL A, Rn | A A EXOR Rn | 1 | 1
XRL A, direct | A A EXOR (direct) | 1 | 1
XRL A, @Ri | A A EXOR @Ri | 2 | 1
XRL A, #data | A A EXOR data | 1 | 1
XRL direct, A | (direct) (direct) EXOR A | 2 | 1
XRL direct, #data | (direct) (direct) EXOR data | 3 | 2
Logical instructions

## Slide 34
MOV @Ri, direct | @Ri (direct) | 2 | 2
MOV @Ri, #data | @Ri data | 2 | 1
MOV DPTR, #data16 | DPTR data16 | 3 | 2
MOVC A, @A+DPTR | A Code byte pointed by A + DPTR | 1 | 2
MOVC A, @A+PC | A Code byte pointed by A + PC | 1 | 2
MOVC A, @Ri | A Code byte pointed by Ri 8-bit address) | 1 | 2
MOVX A, @DPTR | A External data pointed by DPTR | 1 | 2
MOVX @Ri, A | @Ri A (External data - 8bit address) | 1 | 2
MOVX @DPTR, A | @DPTR A(External data - 16bit address) | 1 | 2
PUSH direct | (SP) (direct) | 2 | 2
POP direct | (direct) (SP) | 2 | 2
XCH Rn | Exchange A with Rn | 1 | 1
XCH direct | Exchange A with direct byte | 2 | 1
XCH @Ri | Exchange A with indirect RAM | 1 | 1
XCHD A, @Ri | Exchange least significant nibble of A with that of indirect RAM | 1 | 1
Data transfer instructions
MOV A, Rn | A Rn | 1 | 1
MOV A, direct | A (direct) | 2 | 1
MOV A, @Ri | A @Ri | 1 | 1
MOV A, #data | A data | 2 | 1
MOV Rn, A | Rn A | 1 | 1
MOV Rn, direct | Rn (direct) | 2 | 2
MOV Rn, #data | Rn data | 2 | 1
MOV direct, A | (direct) A | 2 | 1
MOV direct, Rn | (direct) Rn | 2 | 2
MOV direct1, direct2 | (direct1) (direct2) | 3 | 2
MOV direct, @Ri | (direct) @Ri | 2 | 2
MOV direct, #data | (direct) #data | 3 | 2
MOV @Ri, A | @Ri A | 1 | 1
MOV @Ri, direct | @Ri (direct) | 2 | 2
MOV @Ri, #data | @Ri data | 2 | 1

## Slide 35
Mnemonics | Description | Bytes | Instruction Cycles
CLR C | C-bit 0 | 1 | 1
CLR bit | bit 0 | 2 | 1
SET C | C 1 | 1 | 1
SET bit | bit 1 | 2 | 1
CPL C | C | 1 | 1
CPL bit | bit | 2 | 1
ANL C, /bit | C C . | 2 | 1
ANL C, bit | C C. bit | 2 | 1
ORL C, /bit | C C + | 2 | 1
ORL C, bit | C C + bit | 2 | 1
MOV C, bit | C bit | 2 | 1
MOV bit, C | bit C | 2 | 2
Boolean variable instructions

## Slide 36
JZ rel | If A=0, jump to PC + rel | 2 | 2
JNZ rel | If A ≠ 0 , jump to PC + rel | 2 | 2
LCALL addr16 | PC + 3 (SP), addr16 PC | 3 | 2
LJMP addr 16 | Addr16 PC | 3 | 2
NOP | No operation | 1 | 1
RET | (SP) PC | 1 | 2
RETI | (SP) PC, Enable Interrupt | 1 | 2
SJMP rel | PC + 2 + rel PC | 2 | 2
JMP @A+DPTR | A+DPTR PC | 1 | 2
JZ rel | If A = 0. jump PC+ rel | 2 | 2
JNZ rel | If A ≠ 0, jump PC + rel | 2 | 2
NOP | No operation | 1 | 1
ACALL addr11 | PC + 2 (SP) ; addr 11 PC (7FF) | 2 | 2
AJMP addr11 | Addr11 PC | 2 | 2
CJNE A, direct, rel | Compare with A, jump (PC + rel) if not equal | 3 | 2
CJNE A, #data, rel | Compare with A, jump (PC + rel) if not equal | 3 | 2
CJNE Rn, #data, rel | Compare with Rn, jump (PC + rel) if not equal | 3 | 2
CJNE @Ri, #data, rel | Compare with @Ri A, jump (PC + rel) if not equal | 3 | 2
DJNZ Rn, rel | Decrement Rn, jump if not zero | 2 | 2
DJNZ direct, rel | Decrement (direct), jump if not zero | 3 | 2
JC rel | Jump (PC + rel) if C bit = 1 | 2 | 2
JNC rel | Jump (PC + rel) if C bit = 0 | 2 | 2
JB bit, rel | Jump (PC + rel) if bit = 1 | 3 | 2
JNB bit, rel | Jump (PC + rel) if bit = 0 | 3 | 2
JBC bit, rel | Jump (PC + rel) if bit = 1 | 3 | 2
JMP @A+DPTR | A+DPTR PC | 1 | 2
Program branching instruction
AJMP for Absolute jump within 2k memory
SJMP for short jump within +/-128 bytes from the SJMP Command and
LJMP for Long jump
ACALL allows you to jump to a subroutine within the same 2K page while
LCALL allows you to jump to a subroutine anywhere in the 64K code space.

## Slide 38: Generate square wave on pin P1.0 using timer0 – IS A SOFTWARE APPROACH
MOV TMOD, #01H; SET MODE
LOOP MOV TL0, # 0EEH ; INITIALIZE THE TIMER - 2
MOV TH0, #0FFH; -2
CPL P1.0 – COMPLIMENT BIT - 1
ACALL DELAY – 2
SJMP LOOP - 2
DELAY SET B TR0 ; COUNTING IS ENABLED HERE - 1
AGAIN JNB TF0 AGAIN; LOOKS FOR THE FLAG BIT TF0 - 17
CLR TR0; DISABLE THE COUNTING - 1
CLR TF0 – READY FOR NEXT CYCLE 1
RET 1

## Slide 39: Using Timer 0 interrupt- (keil)
ORG 0000H
LJMP MAIN
ORG 000BH
LJMP SERVICE
ORG 30H
MAIN: MOV TMOD, #00000001B ; initialization of Timer 0 in mode 1
MOV TL0, #00H
MOV TH0, #0DCH
MOV IE, #82H; enable timer 0 interrupt
SETB TR0 ; start timer 0
HERE: SJMP HERE
SERVICE: CPL P1.2
MOV TL0, #00H
MOV TH0, #0DCH ; there is no CLR TF0 , because it is
automatically reset when program jumps to the service routine
RETI
END
Interrupt Enable IE (SFR)
Assembler directives
ORG: defines the starting address for the program in program memory
EQU : assigns a numeric value to a symbol identifier
DB: Define a byte. Puts a byte constant at the memory location specified
DW define a word (16 bit data)
DBIT: define a BIT
END: directive to the assembler to stop the assembly process.

## Slide 40: Time Delay Generation and Calculation

## Slide 41: Machine Cycle
For the CPU to execute an instruction takes a certain number of clock cycles.
In the 8051 family, these clock cycles are referred to as machine cycles.
  Ex：RET needs 2 machine cycles
The 8051 has an on-chip oscillator which generates machine cycles.
The 8051 requires an external clock（a quartz crystal oscillator）to run the on-chip oscillator.
Notes: quartz 石英
crystal 水晶
oscillator:振盪器
The pin of 8051 for external clock => look Chapter 4.

## Slide 42: Machine Cycle
The relationship between two oscillators：
  The length of the machine cycle is 12 of the oscillator period.
  The frequency of the machine cycle is 1/12 of the crystal frequency.
The frequency of the external crystal can be vary from 4 MHz to 30MHz.
Very often the 11.0592MHz crystal oscillator is used to make the 8051-based system compatible with the serial port of the IBM PC（See Chapter 10）.

## Slide 43: Example 1
The following shows crystal frequency for three different 8051-
based systems. Find the period of the machine cycle in each case.
11.0592 MHz (b) 16 MHz (C) 20 MHz
Solution:
11.0592/12 = 921.6 KHz
machine cycle is 1/921.6 KHz = 1.085 s (microsecond)
(b) oscillator period = 1/16 MHz = 0.625 s
machine cycle (MC) = 0.625 s ×12 = 0.75 s
(c) 20 MHz/12 = 1.66 MHz
MC = 1/1.66 MHz = 0.60 s

## Slide 44: Example 2
For an 8051 system of 11.0592 MHz, find how long it takes to
execute each of the following instructions.
(a) MOV R3,#55 (b) DEC R3 (c) DJNZ R2, target
(d) LJMP (e) SJMP (f) NOP (g) MUL AB
Solution:
The machine cycle for a system of 11.0952 MHz is 1.085 s.
Table A-1 shows machine cycles for each instructions.
Instruct Machine cycles Time to execute
(a) MOV R3,#55 1 1×1.085 s = 1.085 s
(b) DEC R3 1 1×1.085 s = 1.085 s
(c) DJNZ R2,target 2 2×1.085 s = 2.17 s
(d) LJMP 2 2×1.085 s = 2.17 s
(e) SJMP 2 2×1.085 s = 2.17 s
(f) NOP 1 1×1.085 s = 1.085 s
(g) MUL AB 4 4×1.085 s = 4.34 s

## Slide 45: Example 3
Find the size of the delay in the following program, if the crystal
frequency is 11.0592 MHz.
MOV A,#55H
AGAIN: MOV P1,A
ACALL DELAY
CPL A
SJMP AGAIN
;－－－Time delay Machine Cycle
DELAY: MOV R3,#200 1
HERE: DJNZ R3,HERE 2
RET 2
Solution: Table A-1
The time delay is
[(200 × 2)+1+2] × 1.085 s = 437.252 s.

## Slide 46: Delay Calculation
A delay subroutine consists of two parts
  setting a counter（initialization）
  a loop
Very often we calculate the time delay based on the instructions inside the loop and ignore the clock cycles associated with the instructions outside the loop.
Two way to get a large delay is
  to use NOP（Example 4）
  to use a loop inside a loop（nested loop）（Example 5）

## Slide 47: Example 4
Find the time delay for the following subroutine, assuming a
crystal frequency of 11.0592 MHz.
Machine Cycle
DELAY: MOV R3,#250 1
HERE: NOP 1
NOP 1
NOP 1
NOP 1
DJNZ R3,HERE 2
RET 2
Solution:
the HERE loop ＆ the two instructions outside the loop
{ [250 (1+1+1+1+2)] + 3 } × 1.085 s
= (1500+3) × 1.085 s = 1769.36 s.

## Slide 48: Example 5
For a machine cycle of 1.085 s, find the time delay in the
following subroutine.
DELAY: Machine Cycle
MOV R2,#200 1
AGAIN: MOV R3,#250 1
HERE: NOP 1
NOP 1
DJNZ R3,HERE 2
DJNZ R2,AGAIN 2
RET 2
Solution:
the HERE loop = 250 (1+1+2)=1000 MCs
the AGAIN loop = 200(1000+1+2) =200600 MCs
the whole program = 200600+1+2 = 2006003 MCs
= 200603 × 1.085 s = 217654.255 s

## Slide 49: Square wave of 50% duty cycle
MOV TMOD, #01H; ;SET MODE
LOOP MOV TL0, # 0F2H ; INITIALIZE THE TIMER - 2
MOV TH0, #0FFH; -2
CPL P1.0 – COMPLIMENT BIT - 1
ACALL DELAY – 2
SJMP LOOP - 2
DELAY
SET B TR0 ; COUNTING IS ENABLED HERE - 1
AGAIN JNB TF0 AGAIN ; LOOKS FOR THE FLAG BIT TF0 - 14
CLR TR0 ; DISABLE THE COUNTING - 1
CLR TF0 – READY FOR NEXT CYCLE 1
RET 1
27
T= 2*27*1.085 = 58.59 microsec
F= 1/58.59 microsec = 17067.75 Hz
FFF2…FFF3….FFF4…FFFF…0000 TF=0
0 0 0 1
To find the delay:
F=11.0592/12 = 921.6KHz timer freq
T = 1/F = 1/(921.6 *10^3) = 1.085microsec
FFFF-FFF2 = 0DH =(13)D
FOR ROLL OVER 13+1 = 14
14* 1.085 MICROSEC = 15.19 MICROSEC FOR HALF PULSE
T= 2*15.19 = 30.38 microsec
Delay = no.of counts* 1.085 microsec

## Slide 50: Using Timer 0 interrupt- (keil)
ORG 0000H
LJMP MAIN
ORG 000BH
LJMP SERVICE
ORG 30H
MAIN: MOV TMOD, #00000001B ; initialization of Timer 0 in mode 1
MOV TL0, #00H
MOV TH0, #0DCH
MOV IE, #82H; enable timer 0 interrupt
SETB TR0 ; start timer 0
HERE: SJMP HERE
SERVICE: CPL P1.2
MOV TL0, #00H
MOV TH0, #0DCH ; there is no CLR TF0 , because it is
automatically reset when program jumps to the service routine
RETI
END
Interrupt Enable IE (SFR)
Assembler directives
ORG: defines the starting address for the program in program memory
EQU : assigns a numeric value to a symbol identifier
DB: Define a byte. Puts a byte constant at the memory location specified
DW define a word (16 bit data)
DBIT: define a BIT
END: directive to the assembler to stop the assembly process.

## Slide 51: Delay calculations
To get the maximum delay we make TL0, TH0 = 00
  Delay = (65536 – 0) *1.085 microsec = 71.1065 ms
To generate a pulse width of 5ms on P2.3
  XTAL = 11.0592MHz
  5ms/1.085 microsec = 4608 clocks
  65536 – 4608 = EE00H = 60928
  TL= 00h, TH= EEh
Generate a square wave of 2KHz
  T=2KHz, F = 1/2KHz = 500microsec , half pulse = 1/500 = 250 microsec
  Clocks = 250microsec/1.085microsec = 230
  65536-230 = 65306 = FF1A h
  TL = 1A, TH = FF

## Slide 52: Problems
  Generate a square wave (with 50% duty cycle) of frequency 1, 2, 5, 8, 10, 15, 20 KHz using timer/counter – hardware/ software approach. Assume clock frequency to be 11.0592MHz.
    First get the count corresponding to each frequency.
    Load the registers and verify the frequency/time
  Generate a square wave (with 25% duty cycle) of frequency 1, 2, 5, 8, 10, 15, 20 KHz using timer/counter – hardware/ software approach. Assume clock frequency to be 11.0592MHz.
    Get the count corresponding to 25% and 75% duty cycle
    Load the registers and verify the frequency/time
  Generate a square wave (with 50% duty cycle) of frequency 2 and 4 KHz using Delay. Assume clock frequency to be 11.0592MHz.
  Generate a square wave (with 25% duty cycle) of frequency 2, 4 KHz using Delay. Assume clock frequency to be 11.0592MHz.

## Slide 53: Assignments
Generation of Square, Sine and Triangular Waves using i. hardware (interrupt) and ii. software approaches
To perform 8-bit and 16-bit addition, subtraction, multiplication and division using 8051 Assembly Language
Sorting of numbers in ascending and descending form
To perform Block Transfer and Block Exchange of given data.
Transmit the message serially using i. hardware and ii. software approach.

## Slide 55: TCON
TF1 – Timer 1 over flow flag bit
  8051 it is down counter – FFFF -> 0000 - TF1 will be set to 1
    and will be reset to 0 when the program jumps to the ISS - @ 001BH
  TR1 – timer 1 run control bit
    Counting operation can be controlled by software by setting or resetting this bit
    1 – enable counter
    0 – disable counter
TF0 – Timer 1 over flow flag bit
  In 8051 it is down counter – FFFF -> 0000 - TF0 will be set to 1
    and will be reset to 0 when the program jumps to the ISS - @ 000BH
  TR0 – timer 0 run control bit
    Counting operation can be controlled by software
    1 – enable counter
    0 – disable counter

## Slide 56: USING HARDWARE APPROACH
ORG 0
LJMP MAIN
ORG 000BH ; ISS
CPL P2.0 ; A CLOCK ON PORT 2
RET 1
ORG 0040H
MAIN MOV TMOD, # 02H ; MODE 2
MOV TH0, #92; INITIALIZATION
MOV IE, #82H; INTERRUPT ENABLE
SETB TR0 ; START TIMER
AGAIN MOV A, P1 ; P1 TO A AND SENDING TO PORT 0
MOV P0, A
SJMP AGAIN

## Slide 57
OSC
÷12
TLx
(8 Bit)
THx
(8 Bit)
TFx
(1 Bit)
T Input pin
TR
Gate
INT pin
C= 1 – Counter
C= 0 - timer