## Slide 1: Embedded systems
A system which is a combination of
special purpose hardware and
embedded OS
for executing a
specific set of applications.

## Slide 2: Example real-time and embedded systems
Domain | Application
Avionics | Navigation; displays
Multimedia | Games; simulators
Medicine | Robot surgery; remote surgery; medical imaging
Industrial systems | Robot assembly lines; automated inspection
Civilian | Elevator control Automotive system; Global positioning system (GPS)

## Slide 3: Definition
An embedded system is a computer system with a dedicated function within a larger mechanical or electrical system, often with real-time computing constraints.
It is embedded as part of a complete device often including hardware and mechanical parts.
Embedded systems control many devices in common use today.
Ninety-eight percent of all microprocessors are manufactured as components of embedded systems.
An embedded system is designed to run on its own without human intervention, and may be required to respond to events in real time.

## Slide 4: Features
An embedded system
  is a dedicated computer system designed for one or two specific functions.
  is embedded as a part of a complete device system that includes hardware, such as electrical and mechanical components.
  is unlike the general-purpose computer, which is engineered to manage a wide range of processing tasks.
Because an embedded system is engineered to perform certain tasks only, design engineers may optimize size, cost, power consumption, reliability and performance.
Embedded systems are typically produced on broad scales and. share functionalities across a variety of environments and applications

## Slide 5: Real time Characteristics
RTS have to respond to events in a certain pre-determined amount of time.
  The time constraints have to be considered during planning, design, implementation and testing phases.
Internal failures due to software and hardware fault have be handled satisfactorily.
  You cannot simply pop-up a dialog error box that says “send report” or “don’t send report”.
  Also external failures due to outside sources need to be handled.

## Slide 6: Realtime Characteristics (contd.)
Typical interaction in an RTS is asynchronous.
Thus an RTS should have features to handle asynchronous events such as
  interrupt handlers and
  dispatcher and
  associated resources.
Potential for race condition: when state of resources are timing dependent race condition may occur.
Periodic tasks are common.

## Slide 7: Embedded System
Is a special purpose system designed to perform a few dedicated functions.
Small foot prints (in memory)
Highly optimized code
Cell phones, mp3 players are examples.
The components in an mp3 player are highly optimized for storage operations. (For example, no need to have a floating point operation on an mp3 player!)

## Slide 8: Real-time system concepts
A system is a mapping of a set of input into a set of outputs.
A digital camera is an example of a realtime system: set of input including sensors and imaging devices producing control signals and display information.
Realtime system can be viewed as a sequence of job to be scheduled.
Time between presentation of a set of inputs to a system and the realization of the required behavior, including availability of all associated outputs, is called the response time of the system.

## Slide 9: Real-time system concepts (contd.)
Real-time system is the one in which logical correctness is based on both the correctness of the output as well as their timeliness.
A soft real-time system is one in which performance is degraded by failure to meet response-time constraints.
A hard real-time system is one in which failure to meet a single deadline may lead to complete and catastrophic failure.
More examples:
  Automatic teller: soft
  Robot vacuum cleaner: firm
  Missile delivery system: hard

## Slide 10: Characteristics of embedded systems
Single functioned
Tightly constrained
Reactive and real time

## Slide 11: Design metrics
Non-recurring engineering cost – one time monitory cost of designing
Unit cost – cost/unit (excluding NRE)
Size
Performance – execution time
Power
Flexibility
Ability to change the functionality w/o incurring heavy NRE. S/W is typically considered as very flexible
Type of prototype – used to verify the system’s usefulness and correctness and to rectify the systems functionality
Time to market
Maintainability
Correctness – can be checked at every stage of the design process
Safety

## Slide 12: RTOS Kernel objects
Tasks
Tasks scheduler
Interrupt service routines (ISR)
Semaphores – used for both resource and task synchronization
Mutexes – mutual exclusion – is the general mechanism used for both resource synchronization as well as task synchronization
Mailboxes
Message queues – a data structure used in an OS to pass data between two or more threads
Pipes – task-to-task or ISR-to-task data transfer can take place using pipes
Event registers – a task can have an event register in which the bits correspond to diff events
Signals
Timers – used for measuring elapsed time

## Slide 13: Task and task scheduler

## Slide 14: Real-Time System
Real-time systems have been defined as: “those systems in which the correctness of the system depends not only on the logical result of the computation, but also on the time at which the results are produced“
Correct function at correct time
Usually embedded
Deadlines
  Hard real-time systems
  Soft real-time systems

## Slide 15: Real-Time System continue
Soft RTS: meet timing constraints most of the time, it is not necessary that every time constraint be met. Some deadline miss is tolerated.
Hard RTS: meet all time constraints exactly, Every resource management system must work in the correct order to meet time constraints. No deadline miss is allowed.

## Slide 16: Tasks Categories
Invocation
  Periodic (time-triggered)
  Aperiodic (event-triggered)
Creation
  Static
  Dynamic
Multi-Tasking System
  Preemptive: higher-priority process taking control of the processor from a lower-priority
  Non-Preemptive : Each task can control the CPU for as long as it needs it.

## Slide 17: What is Important in a Scheduling Algorithm?
Minimize Response Time
  Elapsed time to do an operation (job)
  Response time is what the user sees
Maximize Throughput
  Jobs per second
  Throughput related to response time, but not identical
    Minimizing response time will lead to more context switching than if you maximized only throughput
  Minimize overhead (context switch time) as well as efficient use of resources (CPU, disk, memory, etc.)
Fairness
  Share CPU among users in some equitable way
  Not just minimizing average response time

## Slide 18: Why we need scheduling ?!
Each computation (task) we want to execute needs resources like
  processor,
  memory segments,
  communication,
  I/O devices etc.
The computation must be executed in particular order (relative to each other and/or relative to time)
The possible ordering is either completely or statistically a priori known (described)
Scheduling: assignment of processor to computations;
Allocation: assignment of other resources to computations;

## Slide 19: First Come First Serve (FCFS)
Process that requests the CPU FIRST is allocated the CPU FIRST.
Also called FIFO
Implementation
  FIFO queues
  A new process enters at the tail of the queue
  An unblocked process re-enters at the tail of the queue
  The schedule selects from the head of the queue.
Typical performance metric: Average Waiting Time.
Sequence of execution – 4-3-2-1
Task 1 Task 2 Task 3 Task 4
Scheduler

## Slide 20: Problems with FCFS
Non-preemptive
Not optimal AWT
Cannot utilize resources in parallel:
  Assume 1 process CPU bounded and many I/O bounded processes
  Result: Convoy effect, low CPU and I/O Device utilization
  Why?

## Slide 21: Why Convoy Effects?
Consider n-1 jobs in system that are I/O bound and 1 job that is CPU bound.
I/O bound jobs pass quickly through the ready queue and suspend themselves waiting for I/O.
CPU bound job arrives at head of queue and executes until complete.
I/O bound jobs re-join ready queue and wait for CPU bound job to complete.
I/O devices idle until CPU bound job completes.
When CPU bound job completes, other processes rush to wait on I/O again. CPU becomes idle.

## Slide 22: Interactive Scheduling Algorithms
Usually preemptive
  Time is sliced into quantum (time intervals)
  Scheduling decision is also made at the beginning of each quantum
Performance Criteria
  Average response time (AWT)
  Fairness (or proportional resource allocation)
Representative algorithms:
  Priority-based
  Round-robin
  …

## Slide 23: Round-robin
One of the oldest, simplest, most commonly used scheduling algorithm
Select process/thread from ready queue in a round-robin fashion (take turns)
Problems:
Does not consider priority
Context switch overhead

## Slide 24: Round-robin: Example
Process | Duration | Order | Arrival Time
P1 | 3 | 1 | 0
P2 | 4 | 2 | 0
P3 | 3 | 3 | 0
0
Suppose time quantum is: 1 unit, P1, P2 & P3 never block
P1
P2
P3
10
P1
P2
P3
P1
P2
P3
P2
P1 waiting time: 4 (2 [p2,p3]+2[p2,p3])
P2 waiting time: 6 (1 [p1] + 2 [p3,p1] + 2 [p3,p1] + 1 [p3])
P3 waiting time: 6 (2 [p1, p2] + 2 [p1,p2] + 2 [p1,p2] )
The average waiting time (AWT): (4+6+6)/3 = 5.33

## Slide 25: Round-Robin with Priority
Slightly modified by assigning priority levels to some or all the tasks.
The highest priority tasks can interrupt the CPU so that it can be executed.
The scheduling algorithm can meet the desired response time for a higher priority task.

## Slide 26: Shortest Job First (SJF)
Schedule the job with the shortest computation time first
Scheduling in Batch Systems
Two types:
  Non-preemptive multi-tasking
  Preemptive multitasking
Optimal if all jobs are available simultaneously: Gives the best possible AWT (average waiting time)

## Slide 27: Non-preemptive SJF: Example
Process | Duration | Order | Arrival Time
P1 | 6 | 1 | 0
P2 | 8 | 2 | 0
P3 | 7 | 3 | 0
P4 | 3 | 4 | 0
0
3
P4 (3)
P1 (6)
9
P3 (7)
16
P4 waiting time: 0
P1 waiting time: 3
P3 waiting time: 9
P2 waiting time: 16
The total time is: 24
The average waiting time (AWT): (0+3+9+16)/4 = 7
P2 (8)
24

## Slide 28: Comparing to FCFS
Process | Duration | Order | Arrival Time
P1 | 6 | 1 | 0
P2 | 8 | 2 | 0
P3 | 7 | 3 | 0
P4 | 3 | 4 | 0
0
6
P4 (3)
P1 (6)
14
P3 (7)
21
P1 waiting time: 0
P2 waiting time: 6
P3 waiting time: 14
P4 waiting time: 21
The total time is the same.
The average waiting time (AWT): (0+6+14+21)/4 = 10.25
(comparing to 7)
P2 (8)
24

## Slide 29: Preemptive SJF
Shortest job runs first.
A job that arrives and is shorter than the running job will preempt it
A Problem with Preemptive SJF
Starvation
  A job may keep getting preempted by shorter ones
  Example
    Process A with elapse time of 1 hour arrives at time 0
    But every 1 minute, a short process with elapse time of 2 minutes arrives
    Result of SJF: A never gets to run

## Slide 30: ISR – interrupt service routine
Interrupt latency: max time for which interrupts are disabled + time to start the execution of the first instruction in the ISR is called interrupt latency.
Interrupt response time: Time between receipt of interrupt signal and starting the code that handles the interrupt is called IRT
Interrupt recovery time: time required for CPU to return to the interrupted code/higher priority task is called interrupt recovery time.
Interrupt Service Routine Execution
Task running
Task running
Interrupt request
Interrupt Recovery
Time
CPU Context Saving
CPU Context Saving
Interrupt latency
Interrupt Response Time

## Slide 31: Non preemptive
The tasks cooperate each other to get their share of the CPU time
Each task has to release the CPU and give control to another task on its own
Each task is given a priority.
Interrupt Service Routine
Low priority task running
Low priority task running
High priority task running
ISR makes high priority task ready to Run
Low priority task release the CPU
Time

## Slide 32: Preemptive
Highest priority task is always given the CPU time.
If a LP task is presently running and a HP task is in Ready-to-run state, the running task is “preempted” and the HP task is executed
Interrupt Service Routine
High priority task running
Low priority task running
Low priority task running
ISR makes high priority task ready to Run
high priority task release the CPU
Time

## Slide 33: Semaphores: Kernel object that is used for task and resource synchronization
Display
Task 2
Task 1
Task to read the Data
Memory
Task to write the Data
ADC
DAC
Resource synchronization
1. Task 1 acquires semaphore uses display
2. Task 1 releases semaphores
3. Task 2 acquires semaphores
Task 2 uses display
4. Releases semaphore
Semaphore management
Function calls
Create a semaphore 2. Delete a semaphore 3. Acquire a semaphore
4. Release a semaphore 5. Query a semaphore
Task Synchronization

## Slide 34: Mailboxes
Like a postal mailbox used for intertask communication
A task posts a message in the mailbox and another task will read the message
Mailbox
Task
Task
Post a message
Read the message
Function calls
Create a mailbox
delete a mailbox
Query a mailbox
Post a message in a mailbox
Read a message from a mailbox

## Slide 35: Pipes
Used for intertask communication
Function calls in OP API are
  Create a pipe
  Open a pipe
  Close a pipe
  Read from the pipe
  Write to the pipe
Task 1
Task 2

## Slide 36: Message queues
Is an array of mailboxes
Applications of message queues
  Taking the i/p from keyboard
  To display output
  Reading voltages from sensors or transducers
  Data packet transmission in a network
In each of the applications a task or an ISR deposit the message in the message queue
Based on the applications the highest priority task or the first task waiting in the queue can take the message
At the time of creating a queue, the queue is given a
  name or ID,
  queue length,
  sending task waiting list and
  receiving task waiting list
Management function call
Create a queue
Delete a queue
Flush a queue
Post a message in queue
Post a message in front of queue
Read message from queue
Broadcast a message
Show queue information
Show queue waiting list

## Slide 37: Event registers
A task can have an event register in which the bits correspond to different events
16 bit event register
1 0 1 0 1 1 1 1 0 1 1 1 0 1 1 1
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 bit
Task #2
Task #5
Task #4
Task #7
Function call
  Create an event register
  Delete an event register
  Query an event register
  Set an event flag
  Clear an event flag

## Slide 38: Mutex
Mutex is the general mechanism used for both resource synchronization as well as task synchronization
Can be achieved through following mechanism:
  Disabling the scheduler
  Disabling the interrupts
  By test-and-set-operations
  Using semaphore
Mutex management function calls
  Create a mutex
  delete a mutex
  Acquire a mutex
  Release a mutex
  Query a mutex
  Wait on a mutex
Deadlock: occurs when 2 or more tasks wait for resource being held by another task.
  To avoid deadlock a time limit can be set.

## Slide 39: Signals, timer, memory
Signals – to indicate an event
Timers
  Get time
  Set time
  Time delay (in system clock ticks)
  Time delay (in seconds)
  Reset timer
Memory management
  Create a memory block
  Get data from memory
  Post data in the memory
  Query a memory bock
  Free the memory block

## Slide 40: Priority inversion problem
HP task running
LP task running
Low priority task running
Low priority task running
HP wants semaphore held by LP task, HP in waiting state
LP releases Semaphore
LP task Performs operating on SR
MP task running
HP task running
MP, HP tasks waiting for an event to occure
LP gets a semaphore
HP ready to run
MP ready to run
MP completes its work
Priority Inversion

## Slide 41: Priority inheritance
Priority inheritance provides a solution to the problem
When the LP task acquires the mutex, its priority can be increased to a value more than the priority of the HP task.
Kernel has to automatically change this priority
LP task will complete its work very fast and release the mutex which can be acquired by the HP task.
The priority of the task which acquired the mutex will be increased to a value higher than the priority of the task competing for that resources.
LP task gets a semaphore
HP task running
LP task running
HP task running
HP task tries to get semaphore held by LP task priority of LP task raised
LP task releases semaphore
LP task running
LP task running

## Slide 42: Layered architecture of an embedded system
Hardware
Application Software
Application Programming Interface
Operating System Consists of:
Kernel
Communication Hardware
File System
Libraries
Device Manager

## Slide 43: Embedded Applications

## Slide 44: Hardware architecture of an Embedded applications
CPU
Input Device
Output Device
Read-only memory
Random Access memory
Application specific circuitry
Communication interface

## Slide 45: Building blocks of the hardware in an embedded system
Sensors
CPU
ADC
DAC
Power supply unit
Communication Interface
ROM
RAM
Debug Port
LCD
LED’s
Function Keypad
Clock Circuitry
Chip Select
Watchdog timer and rest circuitry

## Slide 46: Recent trends in Embedded Systems
Reliability
Performance
Power consumption
Cost
Size
Limited User Interface
Software up gradation capabilities
Processor Power
Memory
Operating systems
Communication interfaces and networking capabilities
Programming languages
Development tools
Programmable hardware (FPGA)
Specialties of Embedded Systems

## Slide 47: Automated meter reading system

## Slide 48: Digital Clock

## Slide 49: Keyboard Interfacing

## Slide 50
Power supply and
Backlight control interface
Control and Data Interface

## Slide 51: Menu implementation for Digital Clock

## Slide 52: Smart Card Reader
It is a credit card sized plastic card containing memory or a “CPU and Memory”.
It follows a specific command sequence for data read/write operations is controlled by Smartcard Reader/Writer IC.
Based on the interface – two types – contact type and contact less type
Contact type – physical contacts between the reader and the smartcard for communication…
Contact less type - …

## Slide 53: Battery operated Contactless type smartcard reader
Firmware requirements for building the handheld smartcard reader can be divided into the following task:
  Startup task
  Battery monitoring and charge controlling task
  Card read/write operation task
  Communication task
  Keyboard scanning task
  LCD update task
  Watchdog timer expire event

## Slide 54: Smartcard read/write operation follows the sequence:
Initiate the request command for checking the presence of card in the vicinity of the reader – if yes – responds to the reader with Answer to Request (ATR)
Upon receiving the ATR, the reader sends a command to capture the serial no of the card
Reader selects the serial no of a card from the list of SR Nos received and sends a command to select the specified card.
The card whose sr no matches with the one sent by the reader responds to the reader and all other cards enters sleep state.
It establishes the communication channel exclusively between the reader and a card.
The reader authenticates the card with an encrypted key.
The reader sends a read/write command to the card along with the details of the memory area.

## Slide 55: Smart Card Reader

## Slide 56: Digital Camera

## Slide 57: Operating systems

## Slide 58: What’s an Operating System?
Provides environment for executing programs
Process abstraction for multitasking/concurrency
  Scheduling
Hardware abstraction layer (device drivers)
File systems
Communication
We will focus on concurrent, real-time issues

## Slide 59: Operating systems
Off-the-shelf operating systems
Embedded operating systems
Real time operating systems
Handheld operating systems

## Slide 60: Off-the-shelf operating systems
To reduce the development time and effort, it is preferable to use an off-the-shelf OS. Following are the categories
  Non-real-time embedded operating systems
  Real-time operating systems
  Handheld/mobile OS –
    Palm OS,
    Symbian OS
    Windows CE

## Slide 61: Commonalties of the OS
Integrated Development environment (IDE) – to facilitate easy and fast development, vendors supply an IDE that includes editor, complier, debugger and also the necessary cross-platform dev. Tools.
POSIX compatibility: POSIX1003.1-2001 standard specifies the Application Programming Interface to achieve portability of applications.
TCP/IP support:
  TCP/IP protocol stack, including application layer protocols such as FTP, SMTP, HTTP, is integrated along with the OS software.
  Function calls will be provided to access the network-related services.
Device Drivers: No. of device drivers are provided for commonly used devices such as serial ports, parallel port, USB etc.
  A Device Driver kit (DDK) is also generally included that facilitates fast dev of device driver.

## Slide 62: POSIX
The Portable Operating System Interface (POSIX)[1] is a family of standards specified by the IEEE Computer Society for maintaining compatibility between operating systems.
POSIX defines the application programming interface (API), along with command line shells and utility interfaces, for software compatibility with variants of Unix and other operating systems.
This interface is a set of function calls to access the operating system objects and services.

## Slide 63: Embedded OS
Embedded OS use a preemptive priority based kernel, but they do not meet strict deadlines. The stripped-down versions of the desktop OS can be used as embedded OS.
i.e. in the OS software, remove all the unnecessary features and make the kernel occupy a small memory and you have the embedded OS.
This is used in the following three OS:
  Embedded NT
  Windows XP embedded
  Embedded Linux

## Slide 64: RTOS: Role of an OS in Real Time Systems
Standalone Applications
  Often no OS involved
  Micro controller based Embedded Systems
Some Real Time Applications are huge & complex
  Multiple threads
  Complicated Synchronization Requirements
  File system / Network / Windowing support
  OS primitives reduce the software design time

## Slide 65: Background: What’s a “Real Time” System?
When correctness of results depend on content and time
Hard or Soft: indicates how forgiving the system is

## Slide 66: What makes an OS Real-Time?
Predictable (possibly deterministic behavior), that’s all
Not necessarily fast

## Slide 67: How do they work?
Tasks are scheduled by OS according to fixed priority (typically)
Tasks can’t directly interact; they use messages or shared memory & semaphores to communicate

## Slide 68: Designing an RTOS: Typical Features
Many POSIX Specs Exist
No virtual memory (swap file)
Shared memory capabilities
High-resolution timer(s)
Real-time signals/QoS

## Slide 69: Designing an RTOS: End Goal
Have known switching & scheduling overhead
Avoid common problems like priority inversion and deadlock

## Slide 70: Designing an RTOS: Common Problems
Priority inversion
  High-level task stalled due to low-level using shared resources, then a medium-level task holding up the low-level one
  Solution: Priority inheritance – give low-level task high-level priority
  Mars Pathfinder had this problem

## Slide 71: Designing an RTOS: Common Problems (con’t)
Deadlock
  Two semaphores locked out of order by two tasks and circularly block each other
  Solution: “Instant Inheritance” implementation of Priority Ceiling Protocol – semaphores possibly needed by higher processes become priority tokens

## Slide 72: Designing with an RTOS: What do you need?
Task information
  Priorities for each task
  Worst-case runtime
  Best-case period
Interference information
  Deadline Monotonic Analysis (DMA) calculations

## Slide 73: Features of Real Time OS (RTOS)
Scheduling.
Resource Allocation.
Interrupt Handling.
Other issues like kernel size.

## Slide 74: Real-time OS
Few RTOS:
QNx Neutrino
VxWorks
MicroC/OS-II
RTLinux

## Slide 78: Priority Scheduling
Each job is assigned a priority.
FCFS within each priority level.
Select highest priority job over lower ones.
Rational: higher priority jobs are more mission-critical
  Example: DVD movie player vs. send email
Problems:
  May not give the best AWT
  Starvation of lower priority processes

## Slide 79: Priority Scheduling: Example
Process | Duration | Priority | Arrival Time
P1 | 6 | 4 | 0
P2 | 8 | 1 | 0
P3 | 7 | 3 | 0
P4 | 3 | 2 | 0
0
8
P4 (3)
P1 (6)
11
P3 (7)
18
P2 waiting time: 0
P4 waiting time: 8
P3 waiting time: 11
P1 waiting time: 18
The average waiting time (AWT): (0+8+11+18)/4 = 9.25
(worse than SJF)
P2 (8)
24
Do it yourself

## Slide 80: Set Priority
Every process has a default priority
User can also change a process priority
  The nice command

## Slide 81: Set/Get Process Priority
int getpriority(int which, id_t who);
int setpriority(int which, id_t who, int value);

## Slide 83: Real-time Scheduling Taxonomy
Job (Jij): Unit of work, scheduled and executed by system. Jobs repeated at regular or semi-regular intervals modeled as periodic
Task (Ti): Set of related jobs.
Jobs scheduled and allocated resources based on a set of scheduling algorithms and access control protocols.
Scheduler: Module implementing scheduling algorithms
Schedule: assignment of all jobs to available processors, produced by scheduler.
Valid schedule: All jobs meet their deadline
Clock-driven scheduling vs Event(priority)-driven scheduling
Fixed Priority vs Dynamic Priority assignment

## Slide 84: Scheduling Periodic Tasks
In hard real-time systems, set of tasks are known apriori
Task Ti is a series of periodic Jobs Jij. Each task has the following parameters
  ti - period, minimum interrelease interval between jobs in Task Ti.
  ci - maximum execution time for jobs in task Ti.
  rij - release time of the jth Job in Task i (Jij in Ti).
  i - phase of Task Ti, equal to ri1.
  ui - utilization of Task Ti = ci / ti
In addition the following parameters apply to a set of tasks
  H - Hyperperiod = Least Common Multiple of pi for all i: H = lcm(pi), for all i.
  U - Total utilization = Sum over all ui.
Schedulable utilization of an algorithm Us
  If U < Us the set of tasks can be guaranteed to be scheduled

## Slide 85: Real-Time Scheduling Algorithms
Fixed Priority Algorithms
Dynamic Priority Algorithms
Hybrid algorithms
Rate Monotonic scheduling
Deadline Monotonic scheduling
Earliest Deadline First
Least Laxity First
Maximum Urgency First

## Slide 86: Scheduling Algorithm Static vs. Dynamic
Static Scheduling:
  All scheduling decisions at compile time.
    Temporal task structure fixed.
    Precedence and mutual exclusion satisfied by the schedule (implicit synchronization).
    One solution is sufficient.
    Any solution is a sufficient schedulability test.
Benefits
  Simplicity

## Slide 87: Scheduling Algorithm Static vs. Dynamic
Dynamic Scheduling:
  All scheduling decisions at run time.
    Based upon set of ready tasks.
    Mutual exclusion and synchronization enforced by explicit synchronization constructs.
  Benefits
    Flexibility.
    Only actually used resources are claimed.
  Disadvantages
    Guarantees difficult to support
    Computational resources required for scheduling

## Slide 88: Scheduling Algorithm Preemptive vs. Nonpreemptive
Preemptive Scheduling:
  Event driven.
    Each event causes interruption of running tasks.
    Choice of running tasks reconsidered after each interruption.
  Benefits:
    Can minimize response time to events.
  Disadvantages:
    Requires considerable computational resources for scheduling

## Slide 89: Choosing the Time Quantum
Time slice too large
  FIFO behavior
  Poor response time
Time slice too small
  Too many context switches (overheads)
  Inefficient CPU utilization
Heuristic:
  70-80% of jobs block within time-slice
Typical time-slice
  10-100 ms (depends on job priority)