## Slide 1: The ARM Instruction Set
ARM
Advanced RISC Machines

## Slide 2: ARM core dataflow model
Data bus – data enters the processor core through data bus
Instruction decoder – translates instrn before they are executed
Register file – a bank of 32-bit registers used for storing data items
Sign extend – when processor reads signed 8-bit and 16-bit numbers from memory, the sign extend H/w converts these numbers to 32-bit values and then places them in a register file
ALU and MAC unit – reads the operand value from Rn and Rm via A bus and B bus res. Performs the operation and stores the computed result via C bus in Rd and to register file
Address register – holds the address generated by load and store instructions and place it on address bus
Barrel shifter and ALU together can calculate a wide range of expressions and addresses
Incrementer - for load/store instrn the incrementor updates the address register before the core reads or writes next register from or to the next sequential memory locations.
Load – instrn copies data from memory to registers in core
Store – copies data from registers in processor core to memory

## Slide 3: Main features of the ARM Instruction Set
All instructions are 32 bits long.
Most instructions execute in a single cycle.
Every instruction can be conditionally executed.
A load/store architecture
  Data processing instructions act only on registers
    Three operand format
    Combined ALU and shifter for high speed bit manipulation
  Specific memory access instructions with powerful auto-indexing addressing modes.
    32 bit and 8 bit data types
      and also 16 bit data types on ARM Architecture v4.
    Flexible multiple register load and store instructions
Instruction set extension via coprocessors

## Slide 4: Operating Modes
Seven operating modes:
  User
  Privileged:
    System (version 4 and above)
    FIQ
    IRQ
    Abort
    Undefined
    Supervisor
exception modes

## Slide 5: Operating Modes (2)
User mode:
  Normal program execution mode
  System resources unavailable
  Mode changed
  by exception only
Exception modes:
  Entered
  upon exception
  Full access
  to system resources
  Mode changed freely

## Slide 6: Processor Modes
The ARM has six operating modes:
  User (unprivileged mode under which most tasks run)
  FIQ (entered when a high priority (fast) interrupt is raised)
  IRQ (entered when a low priority (normal) interrupt is raised)
  Supervisor (entered on reset and when a Software Interrupt instruction is executed)
  Abort (used to handle memory access violations)
  Undef (used to handle undefined instructions)
ARM Architecture Version 4 adds a seventh mode:
  System (privileged mode using the same registers as user mode)

## Slide 7: Exceptions
Table 1 - Exception types, sorted by Interrupt Vector addresses
Exception | Mode | Priority | IV Address
Reset | Supervisor | 1 | 0x00000000
Undefined instruction | Undefined | 6 | 0x00000004
Software interrupt | Supervisor | 6 | 0x00000008
Prefetch Abort | Abort | 5 | 0x0000000C
Data Abort | Abort | 2 | 0x00000010
Interrupt | IRQ | 4 | 0x00000018
Fast interrupt | FIQ | 3 | 0x0000001C
1 – highest and 6 - lowest

## Slide 8: The Registers
ARM has 37 registers in total, all of which are 32-bits long.
  1 dedicated program counter
  1 dedicated current program status register
  5 dedicated saved program status registers
  30 general purpose registers
However these are arranged into several banks, with the accessible bank being governed by the processor mode. Each mode can access
  a particular set of r0-r12 registers
  a particular r13 (the stack pointer) and r14 (link register)
  r15 (the program counter)
  cpsr (the current program status register)
and privileged modes can also access
  a particular spsr (saved program status register)

## Slide 9: ARM Registers (4)
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13
R14
R15 (PC)
CPSR
System & User
R0
R1
R2
R3
R4
R5
R6
R7
R8_fiq
R9_fiq
R10_fiq
R11_fiq
R12_fiq
R13_fiq
R14_fiq
R15 (PC)
CPSR
SPSR_fiq
FIQ
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13_irq
R14_irq
R15 (PC)
CPSR
SPSR_irq
IRQ
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13_svc
R14_svc
R15 (PC)
CPSR
SPSR_svc
Supervisor
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13_abt
R14_abt
R15 (PC)
CPSR
SPSR_abt
Abort
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13_und
R14_und
R15 (PC)
CPSR
SPSR_und
Undefined

## Slide 10: Register Organization Summary
User mode r0-r7, r15, and cpsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
FIQ
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r0
r1
r2
r3
r4
r5
r6
r7
User
r13 (sp)
r14 (lr)
spsr
IRQ
User mode r0-r12, r15, and cpsr
r13 (sp)
r14 (lr)
spsr
Undef
User mode r0-r12, r15, and cpsr
r13 (sp)
r14 (lr)
spsr
SVC
User mode r0-r12, r15, and cpsr
r13 (sp)
r14 (lr)
spsr
Abort
User mode r0-r12, r15, and cpsr
Thumb state
Low registers
Thumb state
High registers
Note: System mode uses the User mode register set
Notes: This slide shows the registers visible in each mode - basically in a more static fashion than the previous animated slide that is more useful for reference.
The main point to state here is the splitting of the registers in Thumb state into Low and High registers.
ARM register banking is the minimum necessary for fast handling of overlapping exceptions of different types (e.g. ABORT during SWI during IRQ). For nested exceptions of the same type (e.g. re-entrant interrupts) some additional pushing of registers to the stack is required.

## Slide 11: Register Example: User to FIQ Mode
spsr_fiq
cpsr
r7
r4
r5
r2
r1
r0
r3
r6
r15 (pc)
r14_fiq
r13_fiq
r12_fiq
r10_fiq
r11_fiq
r9_fiq
r8_fiq
r14 (lr)
r13 (sp)
r12
r10
r11
r9
r8
User mode CPSR copied to FIQ mode SPSR
cpsr
r15 (pc)
r14 (lr)
r13 (sp)
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r14_fiq
r13_fiq
r12_fiq
r10_fiq
r11_fiq
r9_fiq
r8_fiq
Return address calculated from User mode PC value and stored in FIQ mode LR
Registers in use
Registers in use
EXCEPTION
User Mode
FIQ Mode
spsr_fiq
Notes: Similarly in other 4 modes, though here only r13->r14 swapped.
“Banked” registers stored between mode swaps. Useful for interrupt handling because nothing to set up. Can thus run more quickly.

## Slide 12: The Program Status Registers (CPSR and SPSRs)
Copies of the ALU status flags (latched if the
instruction has the "S" bit set).
N = Negative result from ALU flag.
Z = Zero result from ALU flag.
C = ALU operation Carried out
V = ALU operation oVerflowed
* Interrupt Disable bits.
I = 1, disables the IRQ.
F = 1, disables the FIQ.
* T Bit (Architecture v4T only)
T = 0, Processor in ARM state
T = 1, Processor in Thumb state
* Condition Code Flags
Mode
N
Z
C
V
28
31
8
4
0
I F T
* Mode Bits
M[4:0] define the processor mode.
Notes: Current Program Status Register (CPSR) can be considered as an extension of the PC. It contains the:
  condition code flags, N,Z,C,V.
  interrupt (FIQ, IRQ) disable bits
  mode bits
  T bit
    Software must never change value in TBIT. If this happens, the processor will enter an unpredictable state.
Lower 28 bits known as the "control bits".
Bits other than the specified interrupt and mode bits are reserved for future processors, and no program should depend on their values.
The condition codes in the CPSR will be preserved or updated depending on the value of the S bit in the instruction.
Some instructions do alter condition flags regardless of “S”, ie CMN, CMP, TST and TEQ (return no other result).
Mode field bigger than needs to be - just history.
Only six modes valid on pre-ARM Architecture v4 chips.
SPSRs
  Also five other PSRs, the Saved Program Status Registers, one for each privilege mode, into which a copy of the CPSR is loaded when an exception occurs.

## Slide 13: Condition Flags
Logical Instruction Arithmetic Instruction
Flag
Negative No meaning Bit 31 of the result has been set
(N=‘1’) Indicates a negative number in
signed operations
Zero Result is all zeroes Result of operation was zero
(Z=‘1’)
Carry After Shift operation Result causes an unsigned carry
(C=‘1’) ‘1’ was left in carry flag
oVerflow No meaning Result was greater than 31 bits
(V=‘1’) is set if an addition, subtraction or compare
produces a signed result bigger than 31 bits.
Notes: N flag SUB r0, r1, r2 where r1<r2
Z flag SUB r0, r1, r2 where r1=r2 (also used for results of logical operations)
C flag ADD r0, r1, r2 where r1+r2>0xFFFFFFFF
V flag ADD r0, r1, r2 where r1+r2>0x7FFFFFFF
(if numbers are signed, ALU sign bit will be corrupted)
(0x7FFFFFF+0x00000001=0x80000000)
(answer okay for unsigned but wrong for signed)

## Slide 14: The Program Counter (R15)
When the processor is executing in ARM state:
  All instructions are 32 bits in length
  All instructions must be word aligned
  Therefore the PC value is stored in bits [31:2] with bits [1:0] equal to zero (as instruction cannot be halfword or byte aligned).
R14 is used as the subroutine link register (LR) and stores the return address when Branch with Link operations are performed, calculated from the PC.
Thus to return from a linked branch
  MOV r15,r14
or
  MOV pc,lr
Notes: PC held in register R15
  Instructions always a word long, so must be aligned with word boundaries. But addresses specified in bytes, so 2 lsbs will be zero.
  ie bits [31:2] store word address, bits [1:0] always zero.
R15 may :
  be specified as the base register (Rn) in Load and Store instructions, allowing PC-relative addressing to be used.
  be the destination register, Rd, for instructions. When the “S” bit is not set the operation overwrites R15 without affecting the CPSR. When the “S” bit is set, in a privileged mode, then SPSR_<mode> is transferred to CPSR at the same time R15 is loaded.

## Slide 15: Word alignment
We've defined a word to mean 4 bytes.
To store a word in byte-addressable memory (i.e. where each element of memory is one byte), you have to break up the 32 bit quantity into 4 bytes.
Thus, if the word was 0x01ab23cd, it's broken up into 0x01, 0xab, 0x23, 0xcd.
You can store this in two ways.
  If it's big endian, than the most significant byte (i.e., 0x01) is stored in the smallest of four consective addresses.
  The data 0xab, 0x23, 0xcx are stored in the following three memory addresses.
  Thus, if you stored the first byte in address 1000, the remaining bytes are stored in addresses 1001, 1002, and 1003.
For little endian, you store the least significant byte (0xcd) in the smallest address (in our example, this is address 1000), then 0x23, 0xab, and 0x01. Thus, it's stored in reverse order.

## Slide 16
Quantity Address divisible by (Binary) address ends in
Byte 1 anything
Halfword (16 bits) 2 0
Word (32 bits) 4 00
Doubleword (64 bits) 8 000

## Slide 17: Exception Handling and the Vector Table
When an exception occurs, the core:
  Copies CPSR into SPSR_<mode>
  Sets appropriate CPSR bits
    If core implements ARM Architecture 4T and is currently in Thumb state, then
      ARM state is entered.
    Mode field bits
    Interrupt disable flags if appropriate.
  Maps in appropriate banked registers
  Stores the “return address” in LR_<mode>
  Sets PC to vector address
To return, exception handler needs to:
  Restore CPSR from SPSR_<mode>
  Restore PC from LR_<mode>
Notes: Exceptions, in order serviced, are:
  Reset - supervisor mode
  Data abort - abort mode
  External Fast Interrupt Request - FIQ mode (eg DMA)
  External Interrupt Request - IRQ mode
  Instruction Prefetch abort - abort mode
  Software Interrupt (SWI)- supervisor mode (typically used to extend operating system)
  Undefined instruction - undefined mode
Only one memory location for each vector
  Each vector contains branch to that particular exception handler
  FIQ vector is last one. This allows its handler to be run sequentially from that address, removing need for branch and its associated delays. Important because speed is essential for FIQ.
Interrupt routine’s responsibility to clear interrupt condition.
Can return using one instruction
  See exception handling module for details.

## Slide 18: The Instruction Pipeline
The ARM uses a pipeline in order to increase the speed of the flow of instructions to the processor.
  Allows several operations to be undertaken simultaneously, rather than serially.
Rather than pointing to the instruction being executed, the PC points to the instruction being fetched.
FETCH
DECODE
EXECUTE
Instruction fetched from memory
Decoding of registers used in instruction
Register(s) read from Register Bank
Shift and ALU operation
Write register(s) back to Register Bank
PC
PC - 4
PC - 8
ARM
Notes: Each instruction is one word (or 32 bits)
  Thus each stage in pipeline is one word
  In other words 4 bytes, hence the offsets of 4 and 8 used here.
Most instructions execute in a single cycle
  Helps to keep the pipeline operating efficiently - only stalls if executing instruction takes several cycles.
  Thus every cycle, processor can be loading one instruction, decoding another, whilst executing a third.
Typically the PC can be assumed to be current instruction plus 8
  Cases when not case include
    When exceptions taken the address stored in LR varies - see Exception Handling module for more details.
    When PC used in some data processing operations value is unpredictable - see datasheet

## Slide 19: Instruction Set
Two instruction sets:
  ARM
    Standard 32-bit instruction set
  THUMB
    16-bit compressed form
    Code density better than most CISC
    Dynamic decompression in pipeline

## Slide 20: ARM Instruction Set
Features:
  Load/Store architecture
  3-address data processing instructions
  Conditional execution
  Load/Store multiple registers
  Shift & ALU operation in single clock cycle

## Slide 21: ARM Instruction Set (3)
ARM instruction set
Data processing
instructions
Data transfer
instructions
Software interrupt
instructions
Block transfer
instructions
Multiply instructions
Branching instructions

## Slide 22: ARM Instruction Set (2)
Conditional execution:
  Each data processing instruction
  prefixed by condition code
  Result – smooth flow of instructions through pipeline
  16 condition codes:
EQ | equal | MI | negative | HI | unsigned higher | GT | signed greater than
NE | not equal | PL | positive or zero | LS | unsigned lower or same | LE | signed less than or equal
CS | unsigned higher or same | VS | overflow | GE | signed greater than or equal | AL | always
CC | unsigned lower | VC | no overflow | LT | signed less than | NV | special purpose

## Slide 23: Condition Codes
Not equal
Unsigned higher or same
Unsigned lower
Minus
Equal
Overflow
No overflow
Unsigned higher
Unsigned lower or same
Positive or Zero
Less than signed <
Greater than signed >
Less than or equal signed<=
Always
Greater or equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N=!V
The possible condition codes are listed below:
    Note AL is the default and does not need to be specified
(unsigned >= )
(unsigned < )
Signed >=
Notes: Condition codes are simply a way of testing the ALU status flags.

## Slide 26: Conditional Execution and Flags
ARM instructions can be made to execute conditionally by post fixing them with the appropriate condition code field.
  This improves code density and performance by reducing the number of forward branch instructions.
  CMP r3,#0 CMP r3,#0 BEQ skip ADDNE r0,r1,r2 ADD r0,r1,r2
  skip
By default, data processing instructions do not affect the condition code flags but the flags can be optionally set by using “S”. CMP does not need “S”.
  loop … SUBS r1,r1,#1 (SUB r1,r1,#1 ; b-- ) BNE loop
if Z flag clear then branch
decrement r1 and set flags
Notes: Unusual but powerful feature of the ARM instruction set. Other architectures normally only have conditional branches.
Some recently-added ARM instructions (in v5T and v5TE) are not conditional (e.g. v5T BLX offset)
Core compares condition field in instruction against NZCV flags to determine if instruction should be executed.

## Slide 27: Examples of conditional execution
Use a sequence of several conditional instructions
  if (a==0) func(1);
    CMP r0,#0 MOVEQ r0,#1 BLEQ func
Set the flags, then use various condition codes
  if (a==0) x=0; if (a>0) x=1;
    CMP r0,#0 MOVEQ r1,#0 MOVGT r1,#1
Notes: Sequence of conditional instructions:
- no instruction must reset cond code flags
- BL corrupts flags so must be last
- limit sequence to max 3 or so instrs
Can use different condition codes. Give if then else example. Note GCD practical coming later.
Conditional compare
- resets condition code when executed
- compiler will make use of this
- can be difficult for a human to understand!
Not just for compare, using data processing with condition code and S bit is useful in some circumstances.
LDM/LDR instruction cannot set flags due to datapath issues (data comes back only at the very end of the cycle, so there is no opportunity to perform a comparison and set the status flags).

## Slide 28: example
  Option 1
  gcd CMP r0, r1
  BEQ end
  BLT less
  SUBS r0, r0, r1 ; could be SUB r0, r0, r1 for ARM
  B gcd
  less SUBS r1, r1, r0 ; could be SUB r1, r1, r0 for ARM
  B gcd
  End
  Gcd CMP r0, r1
  SUBGT r0, r0, r1
  SUBLE r1, r1, r0
  BNE gcd
int gcd(int a, int b)
  {
  while (a != b)
  {
  if (a > b)
  a = a - b;
  else
  b = b - a;
  }
  return a;
  }

## Slide 29: Branch instruction
B label : branch unconditionally to label
BCC label : branch to label if carry flag is clear
BEQ label : branch to label if zero flag is set
BL function : subroutine call to function

## Slide 30: Branch and link
STMFD – pushes registers onto the stack – save work and link register
LDMFD – restore work and link register

## Slide 31: Data processing instructions

## Slide 32: Data processing instructions
Operations are:
  ADD operand1 + operand2
  ADC operand1 + operand2 + carry
  SUB operand1 - operand2
  SBC operand1 - operand2 + carry -1
  RSB operand2 - operand1
  RSC operand2 - operand1 + carry - 1
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples
  ADD r0, r1, r2
  SUBGT r3, r3, #1
  RSBLES r4, r5, #5
        subtracts another 1 if the carry flag is clear

## Slide 33: SBC
Given two's complement, subtraction can just be transformed into addition:
z = y - x = y + (-x) = y + ~x + 1
which makes it easier to consider how the carry flag is set in that situation, i.e. by
subs:
        z = 0 - 0
        = 0 + ffffffff + 1
        C:z = 1:00000000 // no borrow, C = 1
        z = 0 - 1
        = 0 + fffffffe + 1
        C:z = 0:ffffffff // borrow, C = 0
In the SBC instruction, the carry bit is used to indicate a "borrow",.
        subtracts another 1 if the carry flag is clear

## Slide 34
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples:
  AND r0, r1, r2
  BICEQ r2, r3, #7
  EORS r1,r3,r0

## Slide 35
Operations are:
  MOV operand2
  MVN NOT operand2
Note that these make no use of operand1.
Syntax:
  <Operation>{<cond>}{S} Rd, Operand2
Examples:
  MOV r0, r1
  MOVS r2, #10
  MVNEQ r1,#0

## Slide 36: The Barrel Shifter
The ARM doesn’t have actual shift instructions.
Instead it has a barrel shifter which provides a mechanism to carry out shifts as part of other instructions.
So what operations does the barrel shifter support?

## Slide 38: Barrel Shifter - Left Shift
Shifts left by the specified amount (multiplies by powers of two) e.g.
  LSL #5 = multiply by 32
Logical Shift Left (LSL)
Destination
CF
0
Notes: Effectively x 2n.
  bits of operand shifted left by specified number of bits.
  Zeros are inserted into the right most end of the word
  last bit removed from the left most end placed in carry flag.
LSL #0 does nothing and is the default shift if none is specified.

## Slide 39: Barrel Shifter - Right Shifts
Logical Shift Right
Shifts right by the specified amount (divides by powers of two) e.g.
LSR #5 = divide by 32
Destination
CF
Logical Shift Right
...0
Destination
CF
Arithmetic Shift Right
Sign bit shifted in
Arithmetic Shift Right
Shifts right (divides by powers of two) and preserves the sign bit, for 2's complement operations. e.g.
ASR #5 = divide by 32
Notes: LSR moves each bit of the register (Rm) to the right by the specified amount.
eg / LSR #5
  all bits are moved 5 places to right (i.e. into less significant positions).
  most significant positions then filled with zeros
  least significant five bits of Rm are removed. The last of these five bits becomes the shifter Carry output, and may set the CPSR's C flag (when the ALU operation is in the logical class).
An LSR 0 is translated into an LSR 32, to put bit 31 of the word into the carry flag.
ASR similar to LSR except that
  high bits are filled with bit 31 of Rm (the sign bit) instead of zeros.
  This preserves the sign in 2's complement notation.
eg/
  Divide a 2's complement number 10000010B (or -126) in Ra by 2.
MOV Ra, Ra, ASR #2
  From Ra=10000010B we get RA=11000001B (or - 63)
An ASR #0 is translated into an ASR #32, to propagate bit 31 of the word into every bit in the word as well as the carry flag.

## Slide 40: Barrel Shifter - Rotations
Rotate Right (ROR)
• Similar to an ASR but the bits wrap around as they leave the LSB and appear as the MSB.
e.g. ROR #5
Note the last bit rotated is also used as the Carry Out.
Destination
CF
Rotate Right through Carry
Rotate Right Extended (RRX)
• This operation uses the CPSR C flag as a 33rd bit.
Destination
CF
Rotate Right
Notes: Rotate Right (ROR), and Rotate Right Extended (RRX) operations
  used to manipulate the bits in a register without destroying those bits.
  move each bit of the register (Rm) by the specified amount.
  eg/ ROR #5
    all bits moved 5 places to the right (i.e. into less significant positions).
  However, rather than being discarded the bits shifted out are then rotated back to other high of the register
    in ROR the bit previously at [0] is rotated to the MSB, [31]
    In RRX - Carry flag included as a 33rd bit in the operation. Bit 0 becomes the Carry out, while the C becomes the MSB
RRX actually encoded as ROR #0
  Example of use: in random number generator given in datasheet
.

## Slide 41: Using the Barrel Shifter: The Second Operand
Immediate value
  8 bit number
  Can be rotated right through an even number of positions.
  Assembler will calculate rotate for you from constant.
Register, optionally with shift operation applied.
Shift value can be either be:
  5 bit unsigned integer
  Specified in bottom byte of another register.
Operand 1
Result
ALU
Barrel Shifter
Operand 2

## Slide 42
The only effect of the comparisons is to
  UPDATE THE CONDITION FLAGS. Thus no need to set S bit.
Operations are:
  CMP operand1 - operand2, but result not written
  CMN operand1 + operand2, but result not written
  TST operand1 AND operand2, but result not written
  TEQ operand1 EOR operand2, but result not written
Syntax:
  <Operation>{<cond>} Rn, Operand2
Examples:
  CMP r0, r1
  TSTEQ r2, #5

## Slide 43: Multiplication Instructions
The Basic ARM provides two multiplication instructions.
Multiply
  MUL{<cond>}{S} Rd, Rm, Rs ; Rd = Rm * Rs
Multiply Accumulate - does addition for free
  MLA{<cond>}{S} Rd, Rm, Rs,Rn ; Rd = (Rm * Rs) + Rn
Operands can be considered signed or unsigned
  Up to user to interpret correctly.
Notes: One example of use of MLA is for string to number conversion:
eg/
  Convert string=“123” to value=123
  value = 0
  loop = 0
  len = length of string
  while loop <> len
  c = extract( string, len -loop,1)
  Rm = 10 ^ loop
  Rs = ASC(c) - ASC (‘0’)
  Rd = value
  MLA Rd, Rm, Rs, Rd
  loop = loop + 1
  endwhile

## Slide 44: Multiply-Long and Multiply-Accumulate Long
Instructions are
  MULL which gives Rd:=Rm*Rs (32 bit)
  MLAL which gives Rd:=(Rm*Rs)+Rn (32 bit)
However the full 64 bit of the result now matter (lower precision multiply instructions simply throws top 32bits away)
  Need to specify whether operands are signed or unsigned
Therefore syntax of new instructions are:
  UMULL{<cond>}{S} RdLo,RdHi,Rm,Rs
  UMLAL{<cond>}{S} RdLo,RdHi,Rm,Rs
  SMULL{<cond>}{S} RdLo, RdHi, Rm, Rs
  SMLAL{<cond>}{S} RdLo, RdHi, Rm, Rs
UMULL R1,R4,R2,R3 ; R4,R1:=R2*R3
UMLALS R1,R5,R2,R3 ; R5,R1:=R2*R3+R5,R1 also setting
; condition codes
Notes: Restrictions - will be picked up by the assembler if overlooked:
  RdHi, RdLo and Rm, and combinations of, cannot be same register.
  r15 cannot be used.

## Slide 45: Multiply and divide instructions

## Slide 46: Load / Store Instructions
The ARM is a Load / Store Architecture:
  Does not support memory to memory data processing operations.
  Must move data values into registers before using them.
This might sound inefficient, but in practice isn’t:
  Load data values from memory into registers.
  Process data in registers using a number of data processing instructions which are not slowed down by memory access.
  Store results from registers out to memory.
The ARM has three sets of instructions which interact with main memory. These are:
  Single register data transfer (LDR / STR).
  Block data transfer (LDM/STM).
  Single Data Swap (SWP).
Notes: All instructions other than these can only use values in registers

## Slide 47: Single register data transfer
The basic load and store instructions are:
  Load and Store Word or Byte
    LDR / STR / LDRB / STRB
ARM Architecture Version 4 also adds support for halfwords and signed data.
  Load and Store Halfword
    LDRH / STRH
  Load Signed Byte or Halfword - load value and sign extend it to 32 bits.
    LDRSB / LDRSH
All of these instructions can be conditionally executed by inserting the appropriate condition code after STR / LDR.
  e.g. LDREQB
Syntax:
  <LDR|STR>{<cond>}{<size>} Rd, <address>

## Slide 48: Load and Store Word or Byte: Base Register
The memory location to be accessed is held in a base register
  STR r0, [r1] ; Store contents of r0 to location pointed to ; by contents of r1.
  LDR r2, [r1] ; Load r2 with contents of memory location ; pointed to by contents of r1.
r1
0x200
Base Register
Memory
0x5
0x200
r0
0x5
Source Register for STR
r2
0x5
Destination Register for LDR

## Slide 49: Load and Store Word or Byte: Offsets from the Base Register
As well as accessing the actual location contained in the base register, these instructions can access a location offset from the base register pointer.
This offset can be
  An unsigned 12bit immediate value (ie 0 - 4095 bytes).
  A register, optionally shifted by an immediate value
This can be either added or subtracted from the base register:
  Prefix the offset value or register with ‘+’ (default) or ‘-’.
This offset can be applied:
  before the transfer is made: Pre-indexed addressing
    optionally auto-incrementing the base register, by postfixing the instruction with an ‘!’.
  after the transfer is made: Post-indexed addressing
    causing the base register to be auto-incremented.

## Slide 50: Load and Store Word or Byte: Pre-indexed Addressing
Example: STR r0, [r1,#12]
To store to location 0x1f4 instead use: STR r0, [r1,#-12]
To auto-increment base pointer to 0x20c use: STR r0, [r1, #12]!
If r2 contains 3, access 0x20c by multiplying this by 4:
  STR r0, [r1, r2, LSL #2]
r1
0x200
Base Register
Memory
0x5
0x200
r0
0x5
Source Register for STR
Offset
12
0x20c

## Slide 51: Load and Store Word or Byte: Post-indexed Addressing
Example: STR r0, [r1], #12
To auto-increment the base register to location 0x1f4 instead use:
  STR r0, [r1], #-12
If r2 contains 3, auto-incremenet base register to 0x20c by multiplying this by 4:
  STR r0, [r1], r2, LSL #2
r1
0x200
Original Base Register
Memory
0x5
0x200
r0
0x5
Source Register for STR
Offset
12
0x20c
r1
0x20c
Updated Base Register

## Slide 52: Offsets for Halfword and Signed Halfword / Byte Access
The Load and Store Halfword and Load Signed Byte or Halfword instructions can make use of pre- and post-indexed addressing in much the same way as the basic load and store instructions.
However the actual offset formats are more constrained:
  The immediate value is limited to 8 bits (rather than 12 bits) giving an offset of 0-255 bytes.
  The register form cannot have a shift applied to it.

## Slide 53: Block Data Transfer
Base register used to determine where memory access should occur.
  4 different addressing modes allow increment and decrement inclusive or exclusive of the base register location.
  Base register can be optionally updated following the transfer (by appending it with an ‘!’.
  Lowest register number is always transferred to/from lowest memory location accessed.
These instructions are very efficient for
  Saving and restoring context
    For this useful to view memory as a stack.
  Moving large blocks of data around memory
    For this useful to directly represent functionality of the instructions.

## Slide 54: Block Transfer Instructions
Load/Store Multiple instructions (LDM/STM)
Whole register bank or a subset
copied to memory or restored
with single instruction
R0
R1
R2
R14
R15
Mi
Mi+1
Mi+2
Mi+14
Mi+15
LDM
STM

## Slide 55: Direct functionality of Block Data Transfer
When LDM / STM are not being used to implement stacks, it is clearer to specify exactly what functionality of the instruction is:
  i.e. specify whether to increment / decrement the base pointer, before or after the memory access.
In order to do this, LDM / STM support a further syntax in addition to the stack one:
  STMIA / LDMIA : Increment After
  STMIB / LDMIB : Increment Before
  STMDA / LDMDA : Decrement After
  STMDB / LDMDB : Decrement Before

## Slide 56: LDM / STM operation
Syntax:
  <LDM|STM>{<cond>}<addressing_mode> Rb{!}, <register list>
4 addressing modes:
  LDMIA / STMIA increment after
  LDMIB / STMIB increment before
  LDMDA / STMDA decrement after
  LDMDB / STMDB decrement before
IA
r1
Increasing Address
r4
r0
r1
r4
r0
r1
r4
r0
r1
r4
r0
r10
IB
DA
DB
LDMxx r10, {r0,r1,r4}
STMxx r10, {r0,r1,r4}
Base Register (Rb)
Notes: Always lowest register first.
Always ascending memory address order.
Uses sequential cycles to take advantage of faster access.
‘addressing_mode’ just determines whether up/down with respect to the base pointer and if value at base pointer address is accessed or skipped. It isn’t possible to add any offset to the base pointer.
Note address and registers loaded/stored are the other way around compared with LDM/STM.
Note the base pointer is not loaded or stored, unless it is in the reg list.

## Slide 57: Example: Block Copy
  Copy a block of memory, which is an exact multiple of 12 words long from the location pointed to by r12 to the location pointed to by r13. r14 points to the end of block to be copied.
; r12 points to the start of the source data
; r14 points to the end of the source data
; r13 points to the start of the destination data
loop LDMIA r12!, {r0-r11} ; load 48 bytes
STMIA r13!, {r0-r11} ; and store them
CMP r12, r14 ; check for the end
BNE loop ; and loop until done
  This loop transfers 48 bytes in 31 cycles
  Over 50 Mbytes/sec at 33 MHz
r13
r14
r12
IncreasingMemory
Notes: Using r12, r13 + r14 as pointers leaves r0-r11 for usage in the blockcopy
Would need to have stored r0-r12 plus r14 onto the stack (so can restore original values when copy finished. Also store r13 to known word in memory so can restore that also.
Using Increment After addressing
4 bytes per register (12 registers) => 48 bytes per iteration
LDM - 14 cycles
STM - 13 cycles
CMP - 1 cycle
BNE - 3 cycles
Total = 31 cycles to move 48 bytes

## Slide 58: Swap and Swap Byte Instructions
Atomic operation of a memory read followed by a memory write which moves byte or word quantities between registers and memory.
Syntax:
  SWP{<cond>}{B} Rd, Rm, [Rn]
Rm
Rd
Rn
3
2
1
temp
Memory
Notes: Used to move a byte or word quantity from a source register (Rm) to external memory, located by base register Rn
Stores the old memory contents in the destination register (Rd).
Instruction is indivisible - LOCK output goes high to signify to an external MMU or processors that the instruction is uninterruptable.
SWP is used to implement semaphores providing a mutual exclusion between the processor and other devices trying to access memory - originally added by Acorn for use in a multiprocessor system.
Thus to implement an actual swap of contents make Rd = Rm.
The compiler cannot produce this instruction.

## Slide 59: Stacks
A stack is an area of memory which grows as new data is “pushed” onto the “top” of it, and shrinks as data is “popped” off the top.
Two pointers define the current limits of the stack.
  A base pointer
    used to point to the “bottom” of the stack (the first location).
  A stack pointer
    used to point the current “top” of the stack.
SP BASE
PUSH {1,2,3}
1
2
3
BASE
SP
POP
1
2
Result of pop = 3
BASE
SP

## Slide 60: Stack Operation
Traditionally, a stack grows down in memory, with the last “pushed” value at the lowest address.
The ARM also supports ascending stacks, where the stack structure grows up through memory.
The value of the stack pointer can either:
  Point to the last occupied address (Full stack)
    and so needs pre-decrementing (ie before the push)
  Point to the next occupied address (Empty stack)
    and so needs post-decrementing (ie after the push)
The stack type to be used is given by the postfix to the instruction:
  STMFD / LDMFD : Full Descending stack
  STMFA / LDMFA : Full Ascending stack.
  STMED / LDMED : Empty Descending stack
  STMEA / LDMEA : Empty Ascending stack
Note: ARM Compiler will always use a Full descending stack.

## Slide 61: Stack Examples
STMFD sp!, {r0,r1,r3-r5}
r5
r4
r3
r1
r0
SP
Old SP
STMED sp!, {r0,r1,r3-r5}
r5
r4
r3
r1
r0
SP
Old SP
r5
r4
r3
r1
r0
STMFA sp!, {r0,r1,r3-r5}
SP
Old SP
0x400
0x418
0x3e8
STMEA sp!, {r0,r1,r3-r5}
r5
r4
r3
r1
r0
SP
Old SP
Notes:   Lowest register mapped to lowest memory address.
  ‘!’ causes stack pointer updated in all these cases.

## Slide 62: Stacks and Subroutines
One use of stacks is to create temporary register workspace for subroutines. Any registers that are needed can be pushed onto the stack at the start of the subroutine and popped off again at the end so as to restore them before return to the caller :
STMFD sp!,{r0-r12, lr} ; stack all registers
........ ; and the return address
........
LDMFD sp!,{r0-r12, pc} ; load all the registers
; and return automatically
If the pop instruction also had the ‘S’ bit set (using ‘^’) then the transfer of the PC when in a priviledged mode would also cause the SPSR to be copied into the CPSR (see exception handling module).

## Slide 63: Software Interrupt (SWI)
A SWI causes a software interrupt exception, which provides a mechanism for applications to call operating system routines.
is a user-defined instruction.
Syntax: SWI {<cond>} SWI_number
It causes an exception trap to the SWI hardware vector (thus causing a change to supervisor mode, plus the associated state saving), thus causing the SWI exception handler to be called.
The handler can then examine the comment field of the instruction to decide what operation has been requested.
By making use of the SWI mechanism, an operating system can implement a set of privileged operations which applications running in user mode can request.
Exception | Mode | Priority | IV Address
Reset | Supervisor | 1 | 0x00000000
Undefined instruction | Undefined | 6 | 0x00000004
Software interrupt | Supervisor | 6 | 0x00000008
Prefetch Abort | Abort | 5 | 0x0000000C
Data Abort | Abort | 2 | 0x00000010
Interrupt | IRQ | 4 | 0x00000018
Fast interrupt | FIQ | 3 | 0x0000001C

## Slide 66: Assembly programs
AREA example, CODE, READONLY ; name this block of code
ENTRY ; mark first instruction to execute
START
MOV r0, #05 ; set up the parameters
MOV r1, #10 ;
BL func ; call subroutine
SWI 0x11 ; terminate using SWI and exit and return to debugger
Func ; subroutine first func
ADD r0,r0,r1 ; r0=r0+r1
MOV pc, lr ; return fro subroutine with result in r0
END ; mark end of file

## Slide 67
AREA hello, CODE, READONLY ; name this block of code
SWI_WriteC EQU &0 ; O/P character in r0
SWI_Exit EQU &11 ; finish program
ENTRY ; mark first instruction to execute
START
ADR r2, TEXT ;r2-> “Hello Students!”
LOOP ldrb R0, [R2], #1 ; GET THE NEXT BYTE
cmp r0, #0 ; check for null character
SWINE swi_WRITEc ; if not end print
BNE LOOP
SWI SWI_Exit ; end of execution
TEXT =“Hello Students!”
END ; mark end of file

## Slide 68: ARM Programs

## Slide 70: Software Interrupt (SWI)
In effect, a SWI is a user-defined instruction.
It causes an exception trap to the SWI hardware vector (thus causing a change to supervisor mode, plus the associated state saving), thus causing the SWI exception handler to be called.
The handler can then examine the comment field of the instruction to decide what operation has been requested.
By making use of the SWI mechanism, an operating system can implement a set of privileged operations which applications running in user mode can request.
28
31
24
27
0
Cond 1 1 1 1
Comment field (ignored by Processor)
Condition Field
23

## Slide 71: Assembly programs

## Slide 75: Data Processing Instructions
Arithmetic and logical operations
3-address format:
  Two 32-bit operands
  (op1 is register, op2 is register or immediate)
  32-bit result placed in a register
Barrel shifter for op2 allows full 32-bit shift
within instruction cycle

## Slide 79: Branch instructions (1)
Branch : B{<cond>} label
Branch with Link : BL{<cond>} sub_routine_label
The offset for branch instructions is calculated by the assembler:
  By taking the difference between the branch instruction and the target address minus 8 (to allow for the pipeline).
  This gives a 26 bit offset which is right shifted 2 bits (as the bottom two bits are always zero as instructions are word – aligned) and stored into the instruction encoding.
  This gives a range of ± 32 Mbytes.
28
31
24
0
Cond 1 0 1 L Offset
Condition field
Link bit 0 = Branch
1 = Branch with link
23
25
27
Notes: Branch instructions are PC-relative rather than absolute:
Branch instructions’ encoding contain a signed 2's complement 24 bit offset which is calculated by the assembler from the destination label given in the source code.

## Slide 81: Branch instructions (2)
When executing the instruction, the processor:
  shifts the offset left two bits, sign extends it to 32 bits, and adds it to PC.
Execution then continues from the new PC, once the pipeline has been refilled.
The "Branch with link" instruction implements a subroutine call by writing PC-4 into the LR of the current bank.
  i.e. the address of the next instruction following the branch with link (allowing for the pipeline).
To return from subroutine, simply need to restore the PC from the LR:
  MOV pc, lr
  Again, pipeline has to refill before execution continues.
The "Branch" instruction does not affect LR.
Note: Architecture 4T offers a further ARM branch instruction, BX
  See Thumb Instruction Set Module for details.
Notes: Branch offset must take account of the PC's prefetch offset, which is handled by the assembler
  In effect subtracts 8 before using it : PC normally +8 of what actually executing - pipeline.
The Branch with Link (BL) writes the old PC into the link register (R14) of the current bank.
  Again PC value saved adjusted for the prefetch offset to point to the next instruction after the BL instruction.
    ie saves PC - 4
CPSR has NOT been saved with the PC.
Return using
  MOV pc, lr
Branch Instruction takes 3 cycles because of refilling the pipeline. Similarly on return.

## Slide 82: Data processing Instructions
Largest family of ARM instructions, all sharing the same instruction format.
Contains:
  Arithmetic operations
  Comparisons (no results - just set condition codes)
  Logical operations
  Data movement between registers
Remember, this is a load / store architecture
  These instruction only work on registers, NOT memory.
They each perform a specific operation on one or two operands.
  First operand always a register - Rn
  Second operand sent to the ALU via barrel shifter.

## Slide 83: Arithmetic Operations
Operations are:
  ADD operand1 + operand2
  ADC operand1 + operand2 + carry
  SUB operand1 - operand2
  SBC operand1 - operand2 + carry -1
  RSB operand2 - operand1
  RSC operand2 - operand1 + carry - 1
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples
  ADD r0, r1, r2
  SUBGT r3, r3, #1
  RSBLES r4, r5, #5

## Slide 84: Comparisons
The only effect of the comparisons is to
  UPDATE THE CONDITION FLAGS. Thus no need to set S bit.
Operations are:
  CMP operand1 - operand2, but result not written
  CMN operand1 + operand2, but result not written
  TST operand1 AND operand2, but result not written
  TEQ operand1 EOR operand2, but result not written
Syntax:
  <Operation>{<cond>} Rn, Operand2
Examples:
  CMP r0, r1
  TSTEQ r2, #5

## Slide 85: Logical Operations
Operations are:
  AND operand1 AND operand2
  EOR operand1 EOR operand2
  ORR operand1 OR operand2
  BIC operand1 AND NOT operand2 [ie bit clear]
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples:
  AND r0, r1, r2
  BICEQ r2, r3, #7
  EORS r1,r3,r0

## Slide 86: Data Movement
Operations are:
  MOV operand2
  MVN NOT operand2
Note that these make no use of operand1.
Syntax:
  <Operation>{<cond>}{S} Rd, Operand2
Examples:
  MOV r0, r1
  MOVS r2, #10
  MVNEQ r1,#0

## Slide 87: Second Operand : Shifted Register
The amount by which the register is to be shifted is contained in either:
  the immediate 5-bit field in the instruction
    NO OVERHEAD
    Shift is done for free - executes in single cycle.
  the bottom byte of a register (not PC)
    Then takes extra cycle to execute
    ARM doesn’t have enough read ports to read 3 registers at once.
    Then same as on other processors where shift is separate instruction.
If no shift is specified then a default shift is applied: LSL #0
  i.e. barrel shifter has no effect on value in register.

## Slide 88: Second Operand : Using a Shifted Register
Using a multiplication instruction to multiply by a constant means first loading the constant into a register and then waiting a number of internal cycles for the instruction to complete.
A more optimum solution can often be found by using some combination of MOVs, ADDs, SUBs and RSBs with shifts.
  Multiplications by a constant equal to a ((power of 2) ± 1) can be done in one cycle.
Example: r0 = r1 * 5 Example: r0 = r1 + (r1 * 4)
ï ADD r0, r1, r1, LSL #2
Example: r2 = r3 * 105 Example: r2 = r3 * 15 * 7 Example: r2 = r3 * (16 - 1) * (8 - 1) ï RSB r2, r3, r3, LSL #4 ; r2 = r3 * 15 ï RSB r2, r2, r2, LSL #3 ; r2 = r2 * 7
Notes: Main use for a shifted register is to provide inline multiplication (and division)
  Using one or more instructions with shifted registers.
This can often be quicker than using MUL instruction, though not as flexible.
  Need to know constant at compile / assemble time.
The problem of finding the optimum sequence becomes more difficult as constant becomes larger.
  No known algorithm to solve this problem quickly.
C compiler restricts amount of searching it does in order to minimise impact on compile time
  Has cut-off so that uses normal MUL once number of instructions used in squence passes a limit.
  Sequences could otherwise become very long.

## Slide 89: Second Operand : Immediate Value (1)
There is no single instruction which will load a 32 bit immediate constant into a register without performing a data load from memory.
  All ARM instructions are 32 bits long
  ARM instructions do not use the instruction stream as data.
The data processing instruction format has 12 bits available for operand2
  If used directly this would only give a range of 4096.
Instead it is used to store 8 bit constants, giving a range of 0 - 255.
These 8 bits can then be rotated right through an even number of positions (ie RORs by 0, 2, 4,..30).
  This gives a much larger range of constants that can be directly loaded, though some constants will still need to be loaded from memory.

## Slide 90: Second Operand : Immediate Value (2)
This gives us:
  0 - 255 [0 - 0xff]
  256,260,264,..,1020 [0x100-0x3fc, step 4, 0x40-0xff ror 30]
  1024,1040,1056,..,4080 [0x400-0xff0, step 16, 0x40-0xff ror 28]
  4096,4160, 4224,..,16320 [0x1000-0x3fc0, step 64, 0x40-0xff ror 26]
These can be loaded using, for example:
  MOV r0, #0x40, 26 ; => MOV r0, #0x1000 (ie 4096)
To make this easier, the assembler will convert to this form for us if simply given the required constant:
  MOV r0, #4096 ; => MOV r0, #0x1000 (ie 0x40 ror 26)
The bitwise complements can also be formed using MVN:
  MOV r0, #0xFFFFFFFF ; assembles to MVN r0, #0
If the required constant cannot be generated, an error will be reported.
Notes: mov r0, #256 ; mov r0, #0x100
mov r1, #0x40, 30 ; mov r1, #0x100
mov r2, #1020 ; mov r2, #0x3fc
mov r3, #0xff, 30 ; mov r3, #0x3fc
mov r4, #1024 ; mov r4, #0x400
mov r5, #0x40, 28 ; mov r5, #0x400
mov r6, #4080 ; mov r6, #0xff0
mov r7, #0xff, 28 ; mov r7, #0xff0
mov r8, #4096 ; mov r8, #0x1000
mov r9, #0x40, 26 ; mov r9, #0x1000
mov r10, #16320 ; mov r10, #0x3fc0
mov r11, #0xff, 26 ; mov r11, #0x3fc0

## Slide 91: Loading full 32 bit constants
Although the MOV/MVN mechansim will load a large range of constants into a register, sometimes this mechansim will not generate the required constant.
Therefore, the assembler also provides a method which will load ANY 32 bit constant:
  LDR rd,=numeric constant
If the constant can be constructed using either a MOV or MVN then this will be the instruction actually generated.
Otherwise, the assembler will produce an LDR instruction with a PC-relative address to read the constant from a literal pool.
  LDR r0,=0x42 ; generates MOV r0,#0x42
  LDR r0,=0x55555555 ; generate LDR r0,[pc, offset to lit pool]
As this mechanism will always generate the best instruction for a given case, it is the recommended way of loading constants.
Notes: Literal pools
  These are constant data areas embedded in the code at the end of modules, and between functions if required by the user.

## Slide 92: Multiplication Instructions
The Basic ARM provides two multiplication instructions.
Multiply
  MUL{<cond>}{S} Rd, Rm, Rs ; Rd = Rm * Rs
Multiply Accumulate - does addition for free
  MLA{<cond>}{S} Rd, Rm, Rs,Rn ; Rd = (Rm * Rs) + Rn
Restrictions on use:
  Rd and Rm cannot be the same register
    Can be avoid by swapping Rm and Rs around. This works because multiplication is commutative.
  Cannot use PC.
These will be picked up by the assembler if overlooked.
Operands can be considered signed or unsigned
  Up to user to interpret correctly.
Notes: One example of use of MLA is for string to number conversion:
eg/
  Convert string=“123” to value=123
  value = 0
  loop = 0
  len = length of string
  while loop <> len
  c = extract( string, len -loop,1)
  Rm = 10 ^ loop
  Rs = ASC(c) - ASC (‘0’)
  Rd = value
  MLA Rd, Rm, Rs, Rd
  loop = loop + 1
  endwhile

## Slide 93: Multiplication Implementation
The ARM makes use of Booth’s Algorithm to perform integer multiplication.
On non-M ARMs this operates on 2 bits of Rs at a time.
  For each pair of bits this takes 1 cycle (plus 1 cycle to start with).
  However when there are no more 1’s left in Rs, the multiplication will early-terminate.
Example: Multiply 18 and -1 : Rd = Rm * Rs
Note: Compiler does not use early termination criteria to decide on which order to place operands.
0 0 0 0
0 0 1 0
0 0 0 1
0 0 0 0
0 0 0 0
0 0 0 0
0 0 0 0
0 0 0 0
1 1 1 1
1 1 1 1
1 1 1 1
1 1 1 1
1 1 1 1
1 1 1 1
1 1 1 1
1 1 1 1
Rm
Rs
17 cycles
Rs
Rm
4 cycles
18
-1
18
-1

## Slide 94: Extended Multiply Instructions
M variants of ARM cores contain extended multiplication hardware. This provides three enhancements:
  An 8 bit Booth’s Algorithm is used
    Multiplication is carried out faster (maximum for standard instructions is now 5 cycles).
  Early termination method improved so that now completes multiplication when all remaining bit sets contain
    all zeroes (as with non-M ARMs), or
    all ones.
  Thus the previous example would early terminate in 2 cycles in both cases.
  64 bit results can now be produced from two 32bit operands
    Higher accuracy.
    Pair of registers used to store result.
Notes: Where M variants are Arch v3M and 4.

## Slide 95: Multiply-Long and Multiply-Accumulate Long
Instructions are
  MULL which gives RdHi,RdLo:=Rm*Rs
  MLAL which gives RdHi,RdLo:=(Rm*Rs)+RdHi,RdLo
However the full 64 bit of the result now matter (lower precision multiply instructions simply throws top 32bits away)
  Need to specify whether operands are signed or unsigned
Therefore syntax of new instructions are:
  UMULL{<cond>}{S} RdLo,RdHi,Rm,Rs
  UMLAL{<cond>}{S} RdLo,RdHi,Rm,Rs
  SMULL{<cond>}{S} RdLo, RdHi, Rm, Rs
  SMLAL{<cond>}{S} RdLo, RdHi, Rm, Rs
Not generated by the compiler.
Warning : Unpredictable on non-M ARMs.
Notes: Restrictions - will be picked up by the assembler if overlooked:
  RdHi, RdLo and Rm, and combinations of, cannot be same register.
  r15 cannot be used.

## Slide 96: Load / Store Instructions
The ARM is a Load / Store Architecture:
  Does not support memory to memory data processing operations.
  Must move data values into registers before using them.
This might sound inefficient, but in practice isn’t:
  Load data values from memory into registers.
  Process data in registers using a number of data processing instructions which are not slowed down by memory access.
  Store results from registers out to memory.
The ARM has three sets of instructions which interact with main memory. These are:
  Single register data transfer (LDR / STR).
  Block data transfer (LDM/STM).
  Single Data Swap (SWP).
Notes: All instructions other than these can only use values in registers

## Slide 97: Single register data transfer
The basic load and store instructions are:
  Load and Store Word or Byte
    LDR / STR / LDRB / STRB
ARM Architecture Version 4 also adds support for halfwords and signed data.
  Load and Store Halfword
    LDRH / STRH
  Load Signed Byte or Halfword - load value and sign extend it to 32 bits.
    LDRSB / LDRSH
All of these instructions can be conditionally executed by inserting the appropriate condition code after STR / LDR.
  e.g. LDREQB
Syntax:
  <LDR|STR>{<cond>}{<size>} Rd, <address>

## Slide 98: Load and Store Word or Byte: Base Register
The memory location to be accessed is held in a base register
  STR r0, [r1] ; Store contents of r0 to location pointed to ; by contents of r1.
  LDR r2, [r1] ; Load r2 with contents of memory location ; pointed to by contents of r1.
r1
0x200
Base Register
Memory
0x5
0x200
r0
0x5
Source Register for STR
r2
0x5
Destination Register for LDR

## Slide 99: Load and Store Word or Byte: Offsets from the Base Register
As well as accessing the actual location contained in the base register, these instructions can access a location offset from the base register pointer.
This offset can be
  An unsigned 12bit immediate value (ie 0 - 4095 bytes).
  A register, optionally shifted by an immediate value
This can be either added or subtracted from the base register:
  Prefix the offset value or register with ‘+’ (default) or ‘-’.
This offset can be applied:
  before the transfer is made: Pre-indexed addressing
    optionally auto-incrementing the base register, by postfixing the instruction with an ‘!’.
  after the transfer is made: Post-indexed addressing
    causing the base register to be auto-incremented.

## Slide 100: Load and Store Word or Byte: Pre-indexed Addressing
Example: STR r0, [r1,#12]
To store to location 0x1f4 instead use: STR r0, [r1,#-12]
To auto-increment base pointer to 0x20c use: STR r0, [r1, #12]!
If r2 contains 3, access 0x20c by multiplying this by 4:
  STR r0, [r1, r2, LSL #2]
r1
0x200
Base Register
Memory
0x5
0x200
r0
0x5
Source Register for STR
Offset
12
0x20c

## Slide 101: Load and Store Word or Byte: Post-indexed Addressing
Example: STR r0, [r1], #12
To auto-increment the base register to location 0x1f4 instead use:
  STR r0, [r1], #-12
If r2 contains 3, auto-incremenet base register to 0x20c by multiplying this by 4:
  STR r0, [r1], r2, LSL #2
r1
0x200
Original Base Register
Memory
0x5
0x200
r0
0x5
Source Register for STR
Offset
12
0x20c
r1
0x20c
Updated Base Register

## Slide 102: Load and Stores with User Mode Privilege
When using post-indexed addressing, there is a further form of Load/Store Word/Byte:
  <LDR|STR>{<cond>}{B}T Rd, <post_indexed_address>
When used in a privileged mode, this does the load/store with user mode privilege.
  Normally used by an exception handler that is emulating a memory access instruction that would normally execute in user mode.

## Slide 103: Offsets for Halfword and Signed Halfword / Byte Access
The Load and Store Halfword and Load Signed Byte or Halfword instructions can make use of pre- and post-indexed addressing in much the same way as the basic load and store instructions.
However the actual offset formats are more constrained:
  The immediate value is limited to 8 bits (rather than 12 bits) giving an offset of 0-255 bytes.
  The register form cannot have a shift applied to it.

## Slide 104: Block Data Transfer (1)
Cond 1 0 0 P U S W L Rn Register list
Condition field
Base register
Load/Store bit
0 = Store to memory
1 = Load from memory
Write- back bit
0 = no write-back
1 = write address into base
PSR and force user bit
0 = don’t load PSR or force user mode
1 = load PSR or force user mode
Up/Down bit
0 = Down; subtract offset from base
1 = Up ; add offset to base
Pre/Post indexing bit
0 = Post; add offset after transfer, 1 = Pre ; add offset before transfer
28
31
22
16
0
23
21
15
27
20
19
24
Each bit corresponds to a particular register. For example:
Bit 0 set causes r0 to be transferred.
Bit 0 unset causes r0 not to be transferred.
At least one register must be transferred as the list cannot be empty.
The Load and Store Multiple instructions (LDM / STM) allow betweeen 1 and 16 registers to be transferred to or from memory.
The transferred registers can be either:
  Any subset of the current bank of registers (default).
  Any subset of the user mode bank of registers when in a priviledged mode (postfix instruction with a ‘^’).

## Slide 105: Block Data Transfer (2)
Base register used to determine where memory access should occur.
  4 different addressing modes allow increment and decrement inclusive or exclusive of the base register location.
  Base register can be optionally updated following the transfer (by appending it with an ‘!’.
  Lowest register number is always transferred to/from lowest memory location accessed.
These instructions are very efficient for
  Saving and restoring context
    For this useful to view memory as a stack.
  Moving large blocks of data around memory
    For this useful to directly represent functionality of the instructions.

## Slide 106: Stacks
A stack is an area of memory which grows as new data is “pushed” onto the “top” of it, and shrinks as data is “popped” off the top.
Two pointers define the current limits of the stack.
  A base pointer
    used to point to the “bottom” of the stack (the first location).
  A stack pointer
    used to point the current “top” of the stack.
SP BASE
PUSH {1,2,3}
1
2
3
BASE
SP
POP
1
2
Result of pop = 3
BASE
SP

## Slide 107: Stack Operation
Traditionally, a stack grows down in memory, with the last “pushed” value at the lowest address. The ARM also supports ascending stacks, where the stack structure grows up through memory.
The value of the stack pointer can either:
  Point to the last occupied address (Full stack)
    and so needs pre-decrementing (ie before the push)
  Point to the next occupied address (Empty stack)
    and so needs post-decrementing (ie after the push)
The stack type to be used is given by the postfix to the instruction:
  STMFD / LDMFD : Full Descending stack
  STMFA / LDMFA : Full Ascending stack.
  STMED / LDMED : Empty Descending stack
  STMEA / LDMEA : Empty Ascending stack
Note: ARM Compiler will always use a Full descending stack.

## Slide 108: Stack Examples
STMFD sp!, {r0,r1,r3-r5}
r5
r4
r3
r1
r0
SP
Old SP
STMED sp!, {r0,r1,r3-r5}
r5
r4
r3
r1
r0
SP
Old SP
r5
r4
r3
r1
r0
STMFA sp!, {r0,r1,r3-r5}
SP
Old SP
0x400
0x418
0x3e8
STMEA sp!, {r0,r1,r3-r5}
r5
r4
r3
r1
r0
SP
Old SP
Notes:   Lowest register mapped to lowest memory address.
  ‘!’ causes stack pointer updated in all these cases.

## Slide 109: Stacks and Subroutines
One use of stacks is to create temporary register workspace for subroutines. Any registers that are needed can be pushed onto the stack at the start of the subroutine and popped off again at the end so as to restore them before return to the caller :
STMFD sp!,{r0-r12, lr} ; stack all registers
........ ; and the return address
........
LDMFD sp!,{r0-r12, pc} ; load all the registers
; and return automatically
See the chapter on the ARM Procedure Call Standard in the SDT Reference Manual for further details of register usage within subroutines.
If the pop instruction also had the ‘S’ bit set (using ‘^’) then the transfer of the PC when in a priviledged mode would also cause the SPSR to be copied into the CPSR (see exception handling module).

## Slide 110: Direct functionality of Block Data Transfer
When LDM / STM are not being used to implement stacks, it is clearer to specify exactly what functionality of the instruction is:
  i.e. specify whether to increment / decrement the base pointer, before or after the memory access.
In order to do this, LDM / STM support a further syntax in addition to the stack one:
  STMIA / LDMIA : Increment After
  STMIB / LDMIB : Increment Before
  STMDA / LDMDA : Decrement After
  STMDB / LDMDB : Decrement Before

## Slide 111: Example: Block Copy
  Copy a block of memory, which is an exact multiple of 12 words long from the location pointed to by r12 to the location pointed to by r13. r14 points to the end of block to be copied.
; r12 points to the start of the source data
; r14 points to the end of the source data
; r13 points to the start of the destination data
loop LDMIA r12!, {r0-r11} ; load 48 bytes
STMIA r13!, {r0-r11} ; and store them
CMP r12, r14 ; check for the end
BNE loop ; and loop until done
  This loop transfers 48 bytes in 31 cycles
  Over 50 Mbytes/sec at 33 MHz
r13
r14
r12
IncreasingMemory
Notes: Using r12, r13 + r14 as pointers leaves r0-r11 for usage in the blockcopy
Would need to have stored r0-r12 plus r14 onto the stack (so can restore original values when copy finished. Also store r13 to known word in memory so can restore that also.
Using Increment After addressing
4 bytes per register (12 registers) => 48 bytes per iteration
LDM - 14 cycles
STM - 13 cycles
CMP - 1 cycle
BNE - 3 cycles
Total = 31 cycles to move 48 bytes

## Slide 112: Swap and Swap Byte Instructions
Atomic operation of a memory read followed by a memory write which moves byte or word quantities between registers and memory.
Syntax:
  SWP{<cond>}{B} Rd, Rm, [Rn]
Thus to implement an actual swap of contents make Rd = Rm.
The compiler cannot produce this instruction.
Rm
Rd
Rn
3
2
1
temp
Memory
Notes: Used to move a byte or word quantity from a source register (Rm) to external memory, located by base register Rn
Stores the old memory contents in the destination register (Rd).
Instruction is indivisible - LOCK output goes high to signify to an external MMU or processors that the instruction is uninterruptable.
SWP is used to implement semaphores providing a mutual exclusion between the processor and other devices trying to access memory - originally added by Acorn for use in a multiprocessor system.

## Slide 113: Software Interrupt (SWI)
In effect, a SWI is a user-defined instruction.
It causes an exception trap to the SWI hardware vector (thus causing a change to supervisor mode, plus the associated state saving), thus causing the SWI exception handler to be called.
The handler can then examine the comment field of the instruction to decide what operation has been requested.
By making use of the SWI mechansim, an operating system can implement a set of privileged operations which applications running in user mode can request.
See Exception Handling Module for further details.
28
31
24
27
0
Cond 1 1 1 1
Comment field (ignored by Processor)
Condition Field
23

## Slide 114: Data Processing Instructions
Arithmetic and logical operations
3-address format:
  Two 32-bit operands
  (op1 is register, op2 is register or immediate)
  32-bit result placed in a register
Barrel shifter for op2 allows full 32-bit shift
within instruction cycle

## Slide 115: Data Processing Instructions (2)
Arithmetic operations:
  ADD, ADDC, SUB, SUBC, RSB, RSC
Bit-wise logical operations:
  AND, EOR, ORR, BIC
Register movement operations:
  MOV, MVN
Comparison operations:
  TST, TEQ, CMP, CMN

## Slide 116: Data Processing Instructions (3)
Conditional codes
+
Data processing instructions
+
Barrel shifter
=
Powerful tools for efficient coded programs

## Slide 117: Data Processing Instructions (4)
e.g.:
if (z==1) R1=R2+(R3*4)
compiles to
EQADDS R1,R2,R3, LSL #2
( SINGLE INSTRUCTION ! )

## Slide 118: Data Transfer Instructions
Load/store instructions
Used to move signed and unsigned
Word, Half Word and Byte to and from registers
Can be used to load PC
(if target address is beyond branch instruction range)
LDR | Load Word | STR | Store Word
LDRH | Load Half Word | STRH | Store Half Word
LDRSH | Load Signed Half Word | STRSH | Store Signed Half Word
LDRB | Load Byte | STRB | Store Byte
LDRSB | Load Signed Byte | STRSB | Store Signed Byte

## Slide 119: Block Transfer Instructions
Load/Store Multiple instructions (LDM/STM)
Whole register bank or a subset
copied to memory or restored
with single instruction
R0
R1
R2
R14
R15
Mi
Mi+1
Mi+2
Mi+14
Mi+15
LDM
STM

## Slide 120: Swap Instruction
Exchanges a word between registers
Two cycles
but
single atomic action
Support for RT semaphores
R0
R1
R2
R7
R8
R15

## Slide 121: Modifying the Status Registers
Only indirectly
MSR moves contents from CPSR/SPSR to selected GPR
MRS moves contents from selected GPR to CPSR/SPSR
Only in privileged modes
R0
R1
R7
R8
R14
R15
CPSR
SPSR
MSR
MRS

## Slide 122: Multiply Instructions
Integer multiplication (32-bit result)
Long integer multiplication (64-bit result)
Built in Multiply Accumulate Unit (MAC)
Multiply and accumulate instructions add product to running total

## Slide 123: Multiply Instructions
Instructions:
MUL | Multiply | 32-bit result
MULA | Multiply accumulate | 32-bit result
UMULL | Unsigned multiply | 64-bit result
UMLAL | Unsigned multiply accumulate | 64-bit result
SMULL | Signed multiply | 64-bit result
SMLAL | Signed multiply accumulate | 64-bit result

## Slide 124: Software Interrupt
SWI instruction
  Forces CPU into supervisor mode
  Usage: SWI #n
  Maximum 224 calls
  Suitable for running privileged code and
  making OS calls
Cond
Opcode
Ordinal
31 28 27 24 23 0

## Slide 125: Branching Instructions
Branch (B): jumps forwards/backwards up to 32 MB
Branch link (BL): same + saves (PC+4) in LR
Suitable for function call/return
Condition codes for conditional branches

## Slide 126: Branching Instructions (2)
Branch exchange (BX) and Branch link exchange (BLX): same as B/BL + exchange instruction set (ARM  THUMB)
Only way to swap sets

## Slide 127: Thumb Instruction Set
Compressed form of ARM
  Instructions stored as 16-bit,
  Decompressed into ARM instructions and
  Executed
Lower performance (ARM 40% faster)
Higher density (THUMB saves 30% space)
Optimal – “interworking” (combining two sets) – compiler supported

## Slide 128: THUMB Instruction Set (2)
More traditional:
  No condition codes
  Two-address data processing instructions
Access to R0 – R8 restricted to
  MOV, ADD, CMP
PUSH/POP for stack manipulation
  Descending stack (SP hardwired to R13)

## Slide 129: THUMB Instruction Set (3)
No MSR and MRS, must change to ARM to modify CPSR (change using BX or BLX)
ARM entered automatically after RESET or entering exception mode
Maximum 255 SWI calls

## Slide 130: The Next Step
New ARM Cortex family of processors
  New NEON™ media and signal processing extensions
  Thumb®-2 blended 16/32-bit instruction set for performance and low power
  Improved Interrupt handling

## Slide 131: Summary
Adoption of ARM technology has increased efficiency and lowered costs
ARM is the world’s leading architecture today
  3 billion ARM Powered chips and counting

## Slide 132: ARM Instruction Set Format
Instruction type
Data processing / PSR Transfer
Multiply
Long Multiply (v3M / v4 only)
Swap
Load/Store Byte/Word
Load/Store Multiple
Halfword transfer : Immediate offset (v4 only)
Halfword transfer: Register offset (v4 only)
Branch
Branch Exchange (v4T only)
Coprocessor data transfer
Coprocessor data operation
Coprocessor register transfer
Software interrupt
Cond 0 0 I Opcode S Rn Rd Operand2
Cond 0 0 0 0 0 0 A S Rd Rn Rs 1 0 0 1 Rm
Cond 0 0 0 1 0 B 0 0 Rn Rd 0 0 0 0 1 0 0 1 Rm
Cond 0 1 I P U B W L Rn Rd Offset
Cond 1 0 0 P U S W L Rn Register List
Cond 0 0 0 0 1 U A S RdHi RdLo Rs 1 0 0 1 Rm
Cond 0 0 0 P U 1 W L Rn Rd Offset1 1 S H 1 Offset2
Cond 1 0 1 L Offset
Cond 1 1 0 P U N W L Rn CRd CPNum Offset
Cond 1 1 1 0 Op1 CRn CRd CPNum Op2 0 CRm
Cond 1 1 1 0 Op1 L CRn Rd CPNum Op2 1 CRm
Cond 1 1 1 1 SWI Number
Cond 0 0 0 1 0 0 1 0 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 1 Rn
Cond 0 0 0 P U 0 W L Rn Rd 0 0 0 0 1 S H 1 Rm
31
28
27
16
15
8
7
0

## Slide 133: Conditional Execution
Most instruction sets only allow branches to be executed conditionally.
However by reusing the condition evaluation hardware, ARM effectively increases number of instructions.
  All instructions contain a condition field which determines whether the CPU will execute them.
  Non-executed instructions soak up 1 cycle.
    Still have to complete cycle so as to allow fetching and decoding of following instructions.
This removes the need for many branches, which stall the pipeline (3 cycles to refill).
  Allows very dense in-line code, without branches.
  The Time penalty of not executing several conditional instructions is frequently less than overhead of the branch or subroutine call that would otherwise be needed.

## Slide 134: The Condition Field
28
31
24
20
16
12
8
4
0
Cond
0000 = EQ - Z set (equal)
0001 = NE - Z clear (not equal)
0010 = HS / CS - C set (unsigned higher or same)
0011 = LO / CC - C clear (unsigned lower)
0100 = MI -N set (negative)
0101 = PL - N clear (positive or zero)
0110 = VS - V set (overflow)
0111 = VC - V clear (no overflow)
1000 = HI - C set and Z clear (unsigned higher)
1001 = LS - C clear or Z (set unsigned lower or same)
1010 = GE - N set and V set, or N clear and V clear (>or =)
1011 = LT - N set and V clear, or N clear and V set (>)
1100 = GT - Z clear, and either N set and V set, or N clear and V set (>)
1101 = LE - Z set, or N set and V clear,or N clear and V set (<, or =)
1110 = AL - always
1111 = NV - reserved.
Notes: 4 bit Condition Field refers to the values of the appropriate bits in the CPSR, as indicated on slide.
Most instructions assembled with default condition code "always" (1110, AL).
  This means the instruction will be executed irrespective of the flags in CPSR.
The "never" code (1111, NV) is reserved.
  This family of conditions will be redefined for future use in other ARM devices.
  Use MOV r0, r0 as NOP operation.
Conditional instructions aids code density
  remove need for many branches (discussed earlier)

## Slide 135: Using and updating the Condition Field
To execute an instruction conditionally, simply postfix it with the appropriate condition:
  For example an add instruction takes the form:
    ADD r0,r1,r2 ; r0 = r1 + r2 (ADDAL)
  To execute this only if the zero flag is set:
    ADDEQ r0,r1,r2 ; If zero flag set then… ; ... r0 = r1 + r2
By default, data processing operations do not affect the condition flags (apart from the comparisons where this is the only effect). To cause the condition flags to be updated, the S bit of the instruction needs to be set by postfixing the instruction (and any condition code) with an “S”.
  For example to add two numbers and set the condition flags:
    ADDS r0,r1,r2 ; r0 = r1 + r2 ; ... and set flags

## Slide 136: Branch instructions (1)
Branch : B{<cond>} label
Branch with Link : BL{<cond>} sub_routine_label
The offset for branch instructions is calculated by the assembler:
  By taking the difference between the branch instruction and the target address minus 8 (to allow for the pipeline).
  This gives a 26 bit offset which is right shifted 2 bits (as the bottom two bits are always zero as instructions are word – aligned) and stored into the instruction encoding.
  This gives a range of ± 32 Mbytes.
28
31
24
0
Cond 1 0 1 L Offset
Condition field
Link bit 0 = Branch
1 = Branch with link
23
25
27
Notes: Branch instructions are PC-relative rather than absolute:
Branch instructions’ encoding contain a signed 2's complement 24 bit offset which is calculated by the assembler from the destination label given in the source code.

## Slide 137: Branch instructions (2)
When executing the instruction, the processor:
  shifts the offset left two bits, sign extends it to 32 bits, and adds it to PC.
Execution then continues from the new PC, once the pipeline has been refilled.
The "Branch with link" instruction implements a subroutine call by writing PC-4 into the LR of the current bank.
  i.e. the address of the next instruction following the branch with link (allowing for the pipeline).
To return from subroutine, simply need to restore the PC from the LR:
  MOV pc, lr
  Again, pipeline has to refill before execution continues.
The "Branch" instruction does not affect LR.
Note: Architecture 4T offers a further ARM branch instruction, BX
  See Thumb Instruction Set Module for details.
Notes: Branch offset must take account of the PC's prefetch offset, which is handled by the assembler
  In effect subtracts 8 before using it : PC normally +8 of what actually executing - pipeline.
The Branch with Link (BL) writes the old PC into the link register (R14) of the current bank.
  Again PC value saved adjusted for the prefetch offset to point to the next instruction after the BL instruction.
    ie saves PC - 4
CPSR has NOT been saved with the PC.
Return using
  MOV pc, lr
Branch Instruction takes 3 cycles because of refilling the pipeline. Similarly on return.

## Slide 138: Data processing Instructions
Largest family of ARM instructions, all sharing the same instruction format.
Contains:
  Arithmetic operations
  Comparisons (no results - just set condition codes)
  Logical operations
  Data movement between registers
Remember, this is a load / store architecture
  These instruction only work on registers, NOT memory.
They each perform a specific operation on one or two operands.
  First operand always a register - Rn
  Second operand sent to the ALU via barrel shifter.
We will examine the barrel shifter shortly.

## Slide 139: Arithmetic Operations
Operations are:
  ADD operand1 + operand2
  ADC operand1 + operand2 + carry
  SUB operand1 - operand2
  SBC operand1 - operand2 + carry -1
  RSB operand2 - operand1
  RSC operand2 - operand1 + carry - 1
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples
  ADD r0, r1, r2
  SUBGT r3, r3, #1
  RSBLES r4, r5, #5

## Slide 140: Comparisons
The only effect of the comparisons is to
  UPDATE THE CONDITION FLAGS. Thus no need to set S bit.
Operations are:
  CMP operand1 - operand2, but result not written
  CMN operand1 + operand2, but result not written
  TST operand1 AND operand2, but result not written
  TEQ operand1 EOR operand2, but result not written
Syntax:
  <Operation>{<cond>} Rn, Operand2
Examples:
  CMP r0, r1
  TSTEQ r2, #5

## Slide 141: Logical Operations
Operations are:
  AND operand1 AND operand2
  EOR operand1 EOR operand2
  ORR operand1 OR operand2
  BIC operand1 AND NOT operand2 [ie bit clear]
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples:
  AND r0, r1, r2
  BICEQ r2, r3, #7
  EORS r1,r3,r0

## Slide 142: Data Movement
Operations are:
  MOV operand2
  MVN NOT operand2
Note that these make no use of operand1.
Syntax:
  <Operation>{<cond>}{S} Rd, Operand2
Examples:
  MOV r0, r1
  MOVS r2, #10
  MVNEQ r1,#0

## Slide 143: The Barrel Shifter
The ARM doesn’t have actual shift instructions.
Instead it has a barrel shifter which provides a mechanism to carry out shifts as part of other instructions.
So what operations does the barrel shifter support?

## Slide 144: Barrel Shifter - Left Shift
Shifts left by the specified amount (multiplies by powers of two) e.g.
  LSL #5 = multiply by 32
Logical Shift Left (LSL)
Destination
CF
0
Notes: Effectively x 2n.
  bits of operand shifted left by specified number of bits.
  Zeros are inserted into the right most end of the word
  last bit removed from the left most end placed in carry flag.
LSL #0 does nothing and is the default shift if none is specified.

## Slide 145: Barrel Shifter - Right Shifts
Logical Shift Right
Shifts right by the specified amount (divides by powers of two) e.g.
LSR #5 = divide by 32
Arithmetic Shift Right
Shifts right (divides by powers of two) and preserves the sign bit, for 2's complement operations. e.g.
ASR #5 = divide by 32
Destination
CF
Destination
CF
Logical Shift Right
Arithmetic Shift Right
...0
Sign bit shifted in
Notes: LSR moves each bit of the register (Rm) to the right by the specified amount.
eg / LSR #5
  all bits are moved 5 places to right (i.e. into less significant positions).
  most significant positions then filled with zeros
  least significant five bits of Rm are removed. The last of these five bits becomes the shifter Carry output, and may set the CPSR's C flag (when the ALU operation is in the logical class).
An LSR 0 is translated into an LSR 32, to put bit 31 of the word into the carry flag.
ASR similar to LSR except that
  high bits are filled with bit 31 of Rm (the sign bit) instead of zeros.
  This preserves the sign in 2's complement notation.
eg/
  Divide a 2's complement number 10000010B (or -126) in Ra by 2.
MOV Ra, Ra, ASR #2
  From Ra=10000010B we get RA=11000001B (or - 63)
An ASR #0 is translated into an ASR #32, to propagate bit 31 of the word into every bit in the word as well as the carry flag.

## Slide 146: Barrel Shifter - Rotations
Rotate Right (ROR)
• Similar to an ASR but the bits wrap around as they leave the LSB and appear as the MSB.
e.g. ROR #5
Note the last bit rotated is also used as the Carry Out.
Rotate Right Extended (RRX)
• This operation uses the CPSR C flag as a 33rd bit.
Rotates right by 1 bit. Encoded as ROR #0.
Destination
CF
Rotate Right
Destination
CF
Rotate Right through Carry
Notes: Rotate Right (ROR), and Rotate Right Extended (RRX) operations
  used to manipulate the bits in a register without destroying those bits.
  move each bit of the register (Rm) by the specified amount.
  eg/ ROR #5
    all bits moved 5 places to the right (i.e. into less significant positions).
  However, rather than being discarded the bits shifted out are then rotated back to other high of the register
    in ROR the bit previously at [0] is rotated to the MSB, [31]
    In RRX - Carry flag included as a 33rd bit in the operation. Bit 0 becomes the Carry out, while the C becomes the MSB
RRX actually encoded as ROR #0
  Example of use: in random number generator given in datasheet
.

## Slide 147: Using the Barrel Shifter: The Second Operand
Immediate value
  8 bit number
  Can be rotated right through an even number of positions.
  Assembler will calculate rotate for you from constant.
Register, optionally with shift operation applied.
Shift value can be either be:
  5 bit unsigned integer
  Specified in bottom byte of another register.
Operand 1
Result
ALU
Barrel Shifter
Operand 2

## Slide 148: Second Operand :Shifted Register
The amount by which the register is to be shifted is contained in either:
  the immediate 5-bit field in the instruction
    NO OVERHEAD
    Shift is done for free - executes in single cycle.
  the bottom byte of a register (not PC)
    Then takes extra cycle to execute
    ARM doesn’t have enough read ports to read 3 registers at once.
    Then same as on other processors where shift is separate instruction.
If no shift is specified then a default shift is applied: LSL #0
  i.e. barrel shifter has no effect on value in register.

## Slide 149: Second Operand : Using a Shifted Register
Using a multiplication instruction to multiply by a constant means first loading the constant into a register and then waiting a number of internal cycles for the instruction to complete.
A more optimum solution can often be found by using some combination of MOVs, ADDs, SUBs and RSBs with shifts.
  Multiplications by a constant equal to a ((power of 2) ± 1) can be done in one cycle.
Example: r0 = r1 * 5 Example: r0 = r1 + (r1 * 4)
ï ADD r0, r1, r1, LSL #2
Example: r2 = r3 * 105 Example: r2 = r3 * 15 * 7 Example: r2 = r3 * (16 - 1) * (8 - 1) ï RSB r2, r3, r3, LSL #4 ; r2 = r3 * 15 ï RSB r2, r2, r2, LSL #3 ; r2 = r2 * 7
Notes: Main use for a shifted register is to provide inline multiplication (and division)
  Using one or more instructions with shifted registers.
This can often be quicker than using MUL instruction, though not as flexible.
  Need to know constant at compile / assemble time.
The problem of finding the optimum sequence becomes more difficult as constant becomes larger.
  No known algorithm to solve this problem quickly.
C compiler restricts amount of searching it does in order to minimise impact on compile time
  Has cut-off so that uses normal MUL once number of instructions used in squence passes a limit.
  Sequences could otherwise become very long.

## Slide 150: Second Operand : Immediate Value (1)
There is no single instruction which will load a 32 bit immediate constant into a register without performing a data load from memory.
  All ARM instructions are 32 bits long
  ARM instructions do not use the instruction stream as data.
The data processing instruction format has 12 bits available for operand2
  If used directly this would only give a range of 4096.
Instead it is used to store 8 bit constants, giving a range of 0 - 255.
These 8 bits can then be rotated right through an even number of positions (ie RORs by 0, 2, 4,..30).
  This gives a much larger range of constants that can be directly loaded, though some constants will still need to be loaded from memory.

## Slide 151: Second Operand : Immediate Value (2)
This gives us:
  0 - 255 [0 - 0xff]
  256,260,264,..,1020 [0x100-0x3fc, step 4, 0x40-0xff ror 30]
  1024,1040,1056,..,4080 [0x400-0xff0, step 16, 0x40-0xff ror 28]
  4096,4160, 4224,..,16320 [0x1000-0x3fc0, step 64, 0x40-0xff ror 26]
These can be loaded using, for example:
  MOV r0, #0x40, 26 ; => MOV r0, #0x1000 (ie 4096)
To make this easier, the assembler will convert to this form for us if simply given the required constant:
  MOV r0, #4096 ; => MOV r0, #0x1000 (ie 0x40 ror 26)
The bitwise complements can also be formed using MVN:
  MOV r0, #0xFFFFFFFF ; assembles to MVN r0, #0
If the required constant cannot be generated, an error will be reported.
Notes: mov r0, #256 ; mov r0, #0x100
mov r1, #0x40, 30 ; mov r1, #0x100
mov r2, #1020 ; mov r2, #0x3fc
mov r3, #0xff, 30 ; mov r3, #0x3fc
mov r4, #1024 ; mov r4, #0x400
mov r5, #0x40, 28 ; mov r5, #0x400
mov r6, #4080 ; mov r6, #0xff0
mov r7, #0xff, 28 ; mov r7, #0xff0
mov r8, #4096 ; mov r8, #0x1000
mov r9, #0x40, 26 ; mov r9, #0x1000
mov r10, #16320 ; mov r10, #0x3fc0
mov r11, #0xff, 26 ; mov r11, #0x3fc0

## Slide 152: Loading full 32 bit constants
Although the MOV/MVN mechansim will load a large range of constants into a register, sometimes this mechansim will not generate the required constant.
Therefore, the assembler also provides a method which will load ANY 32 bit constant:
  LDR rd,=numeric constant
If the constant can be constructed using either a MOV or MVN then this will be the instruction actually generated.
Otherwise, the assembler will produce an LDR instruction with a PC-relative address to read the constant from a literal pool.
  LDR r0,=0x42 ; generates MOV r0,#0x42
  LDR r0,=0x55555555 ; generate LDR r0,[pc, offset to lit pool]
As this mechanism will always generate the best instruction for a given case, it is the recommended way of loading constants.
Notes: Literal pools
  These are constant data areas embedded in the code at the end of modules, and between functions if required by the user.

## Slide 153: Multiplication Instructions
The Basic ARM provides two multiplication instructions.
Multiply
  MUL{<cond>}{S} Rd, Rm, Rs ; Rd = Rm * Rs
Multiply Accumulate - does addition for free
  MLA{<cond>}{S} Rd, Rm, Rs,Rn ; Rd = (Rm * Rs) + Rn
Restrictions on use:
  Rd and Rm cannot be the same register
    Can be avoid by swapping Rm and Rs around. This works because multiplication is commutative.
  Cannot use PC.
These will be picked up by the assembler if overlooked.
Operands can be considered signed or unsigned
  Up to user to interpret correctly.
Notes: One example of use of MLA is for string to number conversion:
eg/
  Convert string=“123” to value=123
  value = 0
  loop = 0
  len = length of string
  while loop <> len
  c = extract( string, len -loop,1)
  Rm = 10 ^ loop
  Rs = ASC(c) - ASC (‘0’)
  Rd = value
  MLA Rd, Rm, Rs, Rd
  loop = loop + 1
  endwhile

## Slide 154: Multiplication Implementation
The ARM makes use of Booth’s Algorithm to perform integer multiplication.
On non-M ARMs this operates on 2 bits of Rs at a time.
  For each pair of bits this takes 1 cycle (plus 1 cycle to start with).
  However when there are no more 1’s left in Rs, the multiplication will early-terminate.
Example: Multiply 18 and -1 : Rd = Rm * Rs
Note: Compiler does not use early termination criteria to decide on which order to place operands.
0 0 0 0
0 0 1 0
0 0 0 1
0 0 0 0
0 0 0 0
0 0 0 0
0 0 0 0
0 0 0 0
1 1 1 1
1 1 1 1
1 1 1 1
1 1 1 1
1 1 1 1
1 1 1 1
1 1 1 1
1 1 1 1
Rm
Rs
17 cycles
Rs
Rm
4 cycles
18
-1
18
-1

## Slide 155: Extended Multiply Instructions
M variants of ARM cores contain extended multiplication hardware. This provides three enhancements:
  An 8 bit Booth’s Algorithm is used
    Multiplication is carried out faster (maximum for standard instructions is now 5 cycles).
  Early termination method improved so that now completes multiplication when all remaining bit sets contain
    all zeroes (as with non-M ARMs), or
    all ones.
  Thus the previous example would early terminate in 2 cycles in both cases.
  64 bit results can now be produced from two 32bit operands
    Higher accuracy.
    Pair of registers used to store result.
Notes: Where M variants are Arch v3M and 4.

## Slide 156: Multiply-Long and Multiply-Accumulate Long
Instructions are
  MULL which gives RdHi,RdLo:=Rm*Rs
  MLAL which gives RdHi,RdLo:=(Rm*Rs)+RdHi,RdLo
However the full 64 bit of the result now matter (lower precision multiply instructions simply throws top 32bits away)
  Need to specify whether operands are signed or unsigned
Therefore syntax of new instructions are:
  UMULL{<cond>}{S} RdLo,RdHi,Rm,Rs
  UMLAL{<cond>}{S} RdLo,RdHi,Rm,Rs
  SMULL{<cond>}{S} RdLo, RdHi, Rm, Rs
  SMLAL{<cond>}{S} RdLo, RdHi, Rm, Rs
Not generated by the compiler.
Warning : Unpredictable on non-M ARMs.
Notes: Restrictions - will be picked up by the assembler if overlooked:
  RdHi, RdLo and Rm, and combinations of, cannot be same register.
  r15 cannot be used.

## Slide 157: Load / Store Instructions
The ARM is a Load / Store Architecture:
  Does not support memory to memory data processing operations.
  Must move data values into registers before using them.
This might sound inefficient, but in practice isn’t:
  Load data values from memory into registers.
  Process data in registers using a number of data processing instructions which are not slowed down by memory access.
  Store results from registers out to memory.
The ARM has three sets of instructions which interact with main memory. These are:
  Single register data transfer (LDR / STR).
  Block data transfer (LDM/STM).
  Single Data Swap (SWP).
Notes: All instructions other than these can only use values in registers

## Slide 158: Single register data transfer
The basic load and store instructions are:
  Load and Store Word or Byte
    LDR / STR / LDRB / STRB
ARM Architecture Version 4 also adds support for halfwords and signed data.
  Load and Store Halfword
    LDRH / STRH
  Load Signed Byte or Halfword - load value and sign extend it to 32 bits.
    LDRSB / LDRSH
All of these instructions can be conditionally executed by inserting the appropriate condition code after STR / LDR.
  e.g. LDREQB
Syntax:
  <LDR|STR>{<cond>}{<size>} Rd, <address>

## Slide 159: Load and Store Word or Byte: Base Register
The memory location to be accessed is held in a base register
  STR r0, [r1] ; Store contents of r0 to location pointed to ; by contents of r1.
  LDR r2, [r1] ; Load r2 with contents of memory location ; pointed to by contents of r1.
r1
0x200
Base Register
Memory
0x5
0x200
r0
0x5
Source Register for STR
r2
0x5
Destination Register for LDR

## Slide 160: Load and Store Word or Byte: Offsets from the Base Register
As well as accessing the actual location contained in the base register, these instructions can access a location offset from the base register pointer.
This offset can be
  An unsigned 12bit immediate value (ie 0 - 4095 bytes).
  A register, optionally shifted by an immediate value
This can be either added or subtracted from the base register:
  Prefix the offset value or register with ‘+’ (default) or ‘-’.
This offset can be applied:
  before the transfer is made: Pre-indexed addressing
    optionally auto-incrementing the base register, by postfixing the instruction with an ‘!’.
  after the transfer is made: Post-indexed addressing
    causing the base register to be auto-incremented.

## Slide 161: Load and Store Word or Byte: Pre-indexed Addressing
Example: STR r0, [r1,#12]
To store to location 0x1f4 instead use: STR r0, [r1,#-12]
To auto-increment base pointer to 0x20c use: STR r0, [r1, #12]!
If r2 contains 3, access 0x20c by multiplying this by 4:
  STR r0, [r1, r2, LSL #2]
r1
0x200
Base Register
Memory
0x5
0x200
r0
0x5
Source Register for STR
Offset
12
0x20c

## Slide 162: Load and Store Word or Byte: Post-indexed Addressing
Example: STR r0, [r1], #12
To auto-increment the base register to location 0x1f4 instead use:
  STR r0, [r1], #-12
If r2 contains 3, auto-incremenet base register to 0x20c by multiplying this by 4:
  STR r0, [r1], r2, LSL #2
r1
0x200
Original Base Register
Memory
0x5
0x200
r0
0x5
Source Register for STR
Offset
12
0x20c
r1
0x20c
Updated Base Register

## Slide 163: Load and Stores with User Mode Privilege
When using post-indexed addressing, there is a further form of Load/Store Word/Byte:
  <LDR|STR>{<cond>}{B}T Rd, <post_indexed_address>
When used in a privileged mode, this does the load/store with user mode privilege.
  Normally used by an exception handler that is emulating a memory access instruction that would normally execute in user mode.

## Slide 164: Offsets for Halfword and Signed Halfword / Byte Access
The Load and Store Halfword and Load Signed Byte or Halfword instructions can make use of pre- and post-indexed addressing in much the same way as the basic load and store instructions.
However the actual offset formats are more constrained:
  The immediate value is limited to 8 bits (rather than 12 bits) giving an offset of 0-255 bytes.
  The register form cannot have a shift applied to it.

## Slide 165: Block Data Transfer (2)
The Load and Store Multiple instructions (LDM / STM) allow betweeen 1 and 16 registers to be transferred to or from memory.
Base register used to determine where memory access should occur.
  4 different addressing modes allow increment and decrement inclusive or exclusive of the base register location.
  Base register can be optionally updated following the transfer (by appending it with an ‘!’.
  Lowest register number is always transferred to/from lowest memory location accessed.
These instructions are very efficient for
  Saving and restoring context
    For this useful to view memory as a stack.
  Moving large blocks of data around memory
    For this useful to directly represent functionality of the instructions.

## Slide 166: Stacks
A stack is an area of memory which grows as new data is “pushed” onto the “top” of it, and shrinks as data is “popped” off the top.
Two pointers define the current limits of the stack.
  A base pointer
    used to point to the “bottom” of the stack (the first location).
  A stack pointer
    used to point the current “top” of the stack.
SP BASE
PUSH {1,2,3}
1
2
3
BASE
SP
POP
1
2
Result of pop = 3
BASE
SP

## Slide 167: Stack Operation
Traditionally, a stack grows down in memory, with the last “pushed” value at the lowest address. The ARM also supports ascending stacks, where the stack structure grows up through memory.
The value of the stack pointer can either:
  Point to the last occupied address (Full stack)
    and so needs pre-decrementing (ie before the push)
  Point to the next occupied address (Empty stack)
    and so needs post-decrementing (ie after the push)
The stack type to be used is given by the postfix to the instruction:
  STMFD / LDMFD : Full Descending stack
  STMFA / LDMFA : Full Ascending stack.
  STMED / LDMED : Empty Descending stack
  STMEA / LDMEA : Empty Ascending stack
Note: ARM Compiler will always use a Full descending stack.

## Slide 168: Stack Examples
STMFD sp!, {r0,r1,r3-r5}
r5
r4
r3
r1
r0
SP
Old SP
STMED sp!, {r0,r1,r3-r5}
r5
r4
r3
r1
r0
SP
Old SP
r5
r4
r3
r1
r0
STMFA sp!, {r0,r1,r3-r5}
SP
Old SP
0x400
0x418
0x3e8
STMEA sp!, {r0,r1,r3-r5}
r5
r4
r3
r1
r0
SP
Old SP
Notes:   Lowest register mapped to lowest memory address.
  ‘!’ causes stack pointer updated in all these cases.

## Slide 169: Stacks and Subroutines
One use of stacks is to create temporary register workspace for subroutines. Any registers that are needed can be pushed onto the stack at the start of the subroutine and popped off again at the end so as to restore them before return to the caller :
STMFD sp!,{r0-r12, lr} ; stack all registers
........ ; and the return address
........
LDMFD sp!,{r0-r12, pc} ; load all the registers
; and return automatically
See the chapter on the ARM Procedure Call Standard in the SDT Reference Manual for further details of register usage within subroutines.
If the pop instruction also had the ‘S’ bit set (using ‘^’) then the transfer of the PC when in a priviledged mode would also cause the SPSR to be copied into the CPSR (see exception handling module).

## Slide 170: Direct functionality of Block Data Transfer
When LDM / STM are not being used to implement stacks, it is clearer to specify exactly what functionality of the instruction is:
  i.e. specify whether to increment / decrement the base pointer, before or after the memory access.
In order to do this, LDM / STM support a further syntax in addition to the stack one:
  STMIA / LDMIA : Increment After
  STMIB / LDMIB : Increment Before
  STMDA / LDMDA : Decrement After
  STMDB / LDMDB : Decrement Before

## Slide 171: Example: Block Copy
  Copy a block of memory, which is an exact multiple of 12 words long from the location pointed to by r12 to the location pointed to by r13. r14 points to the end of block to be copied.
; r12 points to the start of the source data
; r14 points to the end of the source data
; r13 points to the start of the destination data
loop LDMIA r12!, {r0-r11} ; load 48 bytes
STMIA r13!, {r0-r11} ; and store them
CMP r12, r14 ; check for the end
BNE loop ; and loop until done
  This loop transfers 48 bytes in 31 cycles
  Over 50 Mbytes/sec at 33 MHz
r13
r14
r12
IncreasingMemory
Notes: Using r12, r13 + r14 as pointers leaves r0-r11 for usage in the blockcopy
Would need to have stored r0-r12 plus r14 onto the stack (so can restore original values when copy finished. Also store r13 to known word in memory so can restore that also.
Using Increment After addressing
4 bytes per register (12 registers) => 48 bytes per iteration
LDM - 14 cycles
STM - 13 cycles
CMP - 1 cycle
BNE - 3 cycles
Total = 31 cycles to move 48 bytes

## Slide 172: Swap and Swap Byte Instructions
Atomic operation of a memory read followed by a memory write which moves byte or word quantities between registers and memory.
Syntax:
  SWP{<cond>}{B} Rd, Rm, [Rn]
Thus to implement an actual swap of contents make Rd = Rm.
The compiler cannot produce this instruction.
Rm
Rd
Rn
3
2
1
temp
Memory
Notes: Used to move a byte or word quantity from a source register (Rm) to external memory, located by base register Rn
Stores the old memory contents in the destination register (Rd).
Instruction is indivisible - LOCK output goes high to signify to an external MMU or processors that the instruction is uninterruptable.
SWP is used to implement semaphores providing a mutual exclusion between the processor and other devices trying to access memory - originally added by Acorn for use in a multiprocessor system.

## Slide 173: Software Interrupt (SWI)
In effect, a SWI is a user-defined instruction.
It causes an exception trap to the SWI hardware vector (thus causing a change to supervisor mode, plus the associated state saving), thus causing the SWI exception handler to be called.
The handler can then examine the comment field of the instruction to decide what operation has been requested.
By making use of the SWI mechansim, an operating system can implement a set of privileged operations which applications running in user mode can request.
See Exception Handling Module for further details.
28
31
24
27
0
Cond 1 1 1 1
Comment field (ignored by Processor)
Condition Field
23

## Slide 175: Register Organisation
General registers and Program Counter
Program Status Registers
r15 (pc)
r14 (lr)
r13 (sp)
r14_svc
r13_svc
r14_irq
r13_irq
r14_abt
r13_abt
r14_undef
r13_undef
User32 / System
FIQ32
Supervisor32
Abort32
IRQ32
Undefined32
cpsr
sprsr_fiq
sprsr_fiq
sprsr_fiq
spsr_abt
spsr_svc
sprsr_fiq
sprsr_fiq
spsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
spsr_irq
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r15 (pc)
r15 (pc)
r15 (pc)
r15 (pc)
r15 (pc)
cpsr
cpsr
cpsr
cpsr
cpsr
r14_fiq
r13_fiq
r12_fiq
r10_fiq
r11_fiq
r9_fiq
r8_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
spsr_undef

## Slide 176: Register Example: User to FIQ Mode
spsr_fiq
cpsr
r7
r4
r5
r2
r1
r0
r3
r6
r15 (pc)
r14_fiq
r13_fiq
r12_fiq
r10_fiq
r11_fiq
r9_fiq
r8_fiq
r14 (lr)
r13 (sp)
r12
r10
r11
r9
r8
User mode CPSR copied to FIQ mode SPSR
cpsr
r15 (pc)
r14 (lr)
r13 (sp)
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r14_fiq
r13_fiq
r12_fiq
r10_fiq
r11_fiq
r9_fiq
r8_fiq
Return address calculated from User mode PC value and stored in FIQ mode LR
Registers in use
Registers in use
EXCEPTION
User Mode
FIQ Mode
spsr_fiq
Notes: Similarly in other 4 modes, though here only r13->r14 swapped.
“Banked” registers stored between mode swaps. Useful for interrupt handling because nothing to set up. Can thus run more quickly.

## Slide 177
MUL and MLA
Multiply and multiply-accumulate (32-bit by 32-bit, bottom 32-bit result).
MUL{cond}{S} Rd, Rm, Rs
MLA{cond}{S} Rd, Rm, Rs, Rn
The MUL instruction multiplies the values from Rm and Rs,
and places the least significant 32 bits of the result in Rd.
The MLA instruction multiplies the values from Rm and Rs,
adds the value from Rn, and places the least significant 32 bits of the result in Rd.

## Slide 178: Effect of endianess
The ARM can be set up to access its data in either little or big endian format.
Little endian:
  Least significant byte of a word is stored in bits 0-7 of an addressed word.
Big endian:
  Least significant byte of a word is stored in bits 24-31 of an addressed word.
This has no real relevance unless data is stored as words and then accessed in smaller sized quantities (halfwords or bytes).
  Which byte / halfword is accessed will depend on the endianess of the system involved.
Notes: Origin - Gulliver’s Travels - Which end of egg should you slice off?
The ARM family can be used in either mode, which is chosen by signal bigend.
Basically, if did hex dump of memory would see values stored in reversed order in comparison to each other.
If stored value as word, then retrieved it as bytes, order retrieved depends on endianess in use.

## Slide 179: Endianess Example
Big-endian
Little-endian
r1 = 0x100
r0 = 0x11223344
31 24 23 16 15 8 7 0
11 22 33 44
31 24 23 16 15 8 7 0
11 22 33 44
31 24 23 16 15 8 7 0
44 33 22 11
31 24 23 16 15 8 7 0
00 00 00 44
31 24 23 16 15 8 7 0
00 00 00 11
r2 = 0x44
r2 = 0x11
STR r0, [r1]
LDRB r2, [r1]
r1 = 0x100
Memory

## Slide 180: Block Data Transfer (1)
Cond 1 0 0 P U S W L Rn Register list
Condition field
Base register
Load/Store bit
0 = Store to memory
1 = Load from memory
Write- back bit
0 = no write-back
1 = write address into base
PSR and force user bit
0 = don’t load PSR or force user mode
1 = load PSR or force user mode
Up/Down bit
0 = Down; subtract offset from base
1 = Up ; add offset to base
Pre/Post indexing bit
0 = Post; add offset after transfer, 1 = Pre ; add offset before transfer
28
31
22
16
0
23
21
15
27
20
19
24
Each bit corresponds to a particular register. For example:
Bit 0 set causes r0 to be transferred.
Bit 0 unset causes r0 not to be transferred.
At least one register must be transferred as the list cannot be empty.
The Load and Store Multiple instructions (LDM / STM) allow betweeen 1 and 16 registers to be transferred to or from memory.
The transferred registers can be either:
  Any subset of the current bank of registers (default).
  Any subset of the user mode bank of registers when in a priviledged mode (postfix instruction with a ‘^’).

## Slide 182: Example Usage of Addressing Modes
Imagine an array, the first element of which is pointed to by the contents of r0.
If we want to access a particular element, then we can use pre-indexed addressing:
  r1 is element we want.
  LDR r2, [r0, r1, LSL #2]
If we want to step through every element of the array, for instance to produce sum of elements in the array, then we can use post-indexed addressing within a loop:
  r1 is address of current element (initially equal to r0).
  LDR r2, [r1], #4
Use a further register to store the address of final element, so that the loop can be correctly terminated.
0
1
2
3
element
0
4
8
12
Memory Offset
r0
Pointer to start of array

## Slide 183: Block Data Transfer (1)
Cond 1 0 0 P U S W L Rn Register list
Condition field
Base register
Load/Store bit
0 = Store to memory
1 = Load from memory
Write- back bit
0 = no write-back
1 = write address into base
PSR and force user bit
0 = don’t load PSR or force user mode
1 = load PSR or force user mode
Up/Down bit
0 = Down; subtract offset from base
1 = Up ; add offset to base
Pre/Post indexing bit
0 = Post; add offset after transfer, 1 = Pre ; add offset before transfer
28
31
22
16
0
23
21
15
27
20
19
24
Each bit corresponds to a particular register. For example:
Bit 0 set causes r0 to be transferred.
Bit 0 unset causes r0 not to be transferred.
At least one register must be transferred as the list cannot be empty.
The Load and Store Multiple instructions (LDM / STM) allow betweeen 1 and 16 registers to be transferred to or from memory.
The transferred registers can be either:
  Any subset of the current bank of registers (default).
  Any subset of the user mode bank of registers when in a priviledged mode (postfix instruction with a ‘^’).

## Slide 184: Load and Stores with User Mode Privilege
When using post-indexed addressing, there is a further form of Load/Store Word/Byte:
  <LDR|STR>{<cond>}{B}T Rd, <post_indexed_address>
When used in a privileged mode, this does the load/store with user mode privilege.
  Normally used by an exception handler that is emulating a memory access instruction that would normally execute in user mode.